## Slide 1: Sequential Logic Design

## Slide 2: Introduction
Combinational Circuits
  Without memory
  Outputs depend only on current inputs
  Output determined after sufficient time has elapsed
Sequential Circuits
  Have memory
  Outputs depend on inputs and previous outputs
  Previous output stored even after waiting

## Slide 3: Steady-State Abstraction
In reality, all real circuits are sequential
  The outputs do not change instantaneously after an input change
A fundamental abstraction of digital design is to reason about steady-state behaviors
  Look at outputs only after sufficient time has elapsed for the system to make its required changes and settle down
  Memory of a system is represented as its state
  Changes in system state are only allowed to occur at specific times

## Slide 4: Simple Sequential Circuits
"remember"
"load"
"data"
"stored value"
"0"
"1"
"stored value"
Two inverters form a static memory cell
  The previous output is stored by passing it back into the system
  Will hold value as long as it has power applied
How to get a new value into the memory cell?
  Selectively break feedback path
  Load new value into cell

## Slide 5: Clocks
Clocks are regular periodic signals
  Clock period is divided into two portions
    When the clock is “high”, also called the duty cycle
    When the clock is “low”
  State changes occur on a clock edge
    When the clock moves from low to high or from high to low

## Slide 6: Edge-Triggered Methodology
Either the rising edge or the falling edge is active
  Determined by implementation
  Does not affect design
Elements change on the active clock edge
  All inputs sampled at the same time
  All inputs must be valid (steady) at the active clock edge
Clocked systems are also called synchronous systems.

## Slide 7: Sequential Logic Design
Combinational logic elements are still used
State elements provide valid inputs to the combinational logic block.
Clock period must be long enough to allow all the signals in the combinational logic block to settle

## Slide 8: Sequential Circuits
Latches
Flip-flops
Registers

## Slide 9: Latches
A latch is a memory element in which the output is equal to the value of the stored state inside the element and the state is changed whenever the appropriate inputs change.

## Slide 10: Set-Reset Latch
Built from cross-coupled NOR gates
Ability to force output to 0 (reset=1) or 1 (set=1)
R
S
Q
Q'

## Slide 11: Set-Reset Latch
Can also be build from cross-coupled NAND gates
  NAND is a universal gate
Ability to force output to 0 (reset=0) or 1 (set=0)
Q
Q'
S'
R'

## Slide 12: State Machines
A sequential circuit is described as a finite-state machine
  A set of states
  A function to determine the next state
  A function to determine the output
    Functions can still be represented by a truth table

## Slide 13: Behavior of the S-R Latch
States: {hold, set, reset, unstable}
Next-State function:
S | R | State
0 | 0 | hold
0 | 1 | 0
1 | 0 | 1
1 | 1 | unstable

## Slide 14: Behavior of the S-R Latch
States: {hold, set, reset, unstable}
Output function:
S | R | Qin | Qout
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | ?
1 | 1 | 1 | ?

## Slide 15: Behavior of the S-R Latch
State Diagram
  States: possible outputs
  Transitions: events that cause the system to change states (inputs)
Q Q' 0 1
Q Q' 1 0
Q Q' 0 0
Q Q' 1 1
SR=00
SR=00
SR=10
SR=01
SR=00
SR=10
SR=00
SR=01
SR=11
SR=11
SR=10
SR=01
SR=01
SR=10
SR=11
possible oscillation between states 00 and 11
SR=11

## Slide 16: Behavior of the S-R Latch
Very difficult to observe R-S latch in the 1-1 state
  One of R or S usually changes first
Ambiguously returns to state 0-1 or 1-0
  A so-called "race condition"
  Or non-deterministic transition
SR=00
SR=00
Q Q' 0 1
Q Q' 1 0
Q Q' 0 0
SR=10
SR=01
SR=00
SR=10
SR=00
SR=01
SR=11
SR=11
SR=01
SR=10
SR=11

## Slide 17: Clocked S-R Latch
In an unclocked circuit the outputs change whenever the inputs change.
R
S
Q
Q'

## Slide 18: Clocked S-R Latch
In a clocked circuit, we control when the inputs are sampled.
clock'
S'
Q'
Q
R'
R
S

## Slide 19: Clocked S-R Latch
clock
R' and S'
changing
stable
changing
stable
stable
Controlling an R-S latch with a clock
  Can't let R and S change while clock is active
  Only have half of clock period for signal changes to propagate
  Signals must be stable for the other half of clock period
clock'
S'
Q'
Q
R'
R
S

## Slide 20: Flip-Flops
A flip-flop is a memory element for which the output is equal to the value of the stored state inside the element and for which the internal state is changed only on a clock edge.
  Often built from clocked latches

## Slide 21: D Flip-Flop
2 Inputs
  D, the data to be stored
  C, the clock signal
2 Outputs
  Q, the internal state
  Q’, the complement of Q

## Slide 22: D Flip-Flop
When the clock is asserted, the flip-flop is “open”
  If D is 1, the S-R latch is “set”
  If D is 0, the S-R latch is “reset”
When the clock is deasserted, the flip-flop is “closed”
  The S-R latch is “holding”

## Slide 23: D Flip-Flop
Flip-Flops can be built to trigger on either the rising or falling clock edge
  Remember this does not affect the design
Flip-Flops can be build to trigger on the offset edge
  If all Flip-Flops trigger on the positive edge, we can build one to trigger on the negative edge
  We use cascading logic blocks

## Slide 24: Cascading Logic Circuits
clock
R
S
Q
Q'
R
S
Q
Q'
R
S
Connect output of one latch to input of another
How to stop changes from racing through chain?
  Need to control flow of data from one latch to the next
  Advance from one latch per clock period

## Slide 25: Master-Slave Structure
Break flow by alternating clocks
  Use positive clock to latch inputs into one S-R latch
  Use negative clock to change outputs with another S-R latch
View pair as one basic unit
  master-slave flip-flop
  twice as much logic
  output changes a few gate delays after the falling edge of clock
master stage
slave stage
CLK
R
S
Q
Q'
R
S
Q
Q'
R
S

## Slide 26: Negative Edge-Triggered Flip-Flops
Q
D
Clk=1
R
S
0
D’
0
D’
D
Q’
More efficient solution: only 6 gates
4-5 gate delays
Must respect setup and hold time constraints to successfully capture input

## Slide 27: Timing Methodologies
The set up time is the minimum time that the input must be valid before the clock edge.
The hold time is the minimum time during which it must be valid after the clock edge.

## Slide 28: Timing Methodologies
Rules for interconnecting components and clocks
  Guarantee proper operation of system when strictly followed
Approach depends on building blocks used for memory elements
  Focus on systems with edge-triggered flip-flops
Basic rules for correct timing:
  (1) Correct inputs, with respect to time, are provided to the flip-flops
  (2) No flip-flop changes state more than once per clocking event

## Slide 29: Typical Timing Specifications
all measurements are made from the clocking event: the rising edge of the clock
Positive edge-triggered D flip-flop
  Setup and hold times
  Minimum clock width
  Propagation delays (low to high, high to low, max and typical)
Th 5ns
Tw 25ns
Tplh 25ns 13ns
Tphl 40ns 25ns
Tsu 20ns
D
CLK
Q
Tsu 20ns
Th 5ns

## Slide 30: Cascading Edge-triggered Flip-Flops
IN
Q0
Q1
CLK
100
Consider setup/hold/propagation delays
  prop must be > hold
CLK
IN
Q0
Q1
D
Q
D
Q
OUT

## Slide 31: Clock Skew
Correct behavior assumes next state of all storage elements determined by all storage elements at the same time
This is difficult in high-performance systems because time for clock to arrive at flip-flop is comparable to delays through logic
Clock skew is the difference in time between when two state elements see a clock edge

## Slide 32: Clock Skew
original state: IN = 0, Q0 = 1, Q1 = 1
due to skew, next state becomes: Q0 = 0, Q1 = 0, and not Q0 = 0, Q1 = 1
CLK1 is a delayed
version of CLK0
In
Q0
Q1
CLK0
CLK1
100
If the clock skew is large enough, it may be possible for a state element to change and cause the input to another flip-flop to change before the clock edge is seen by the second flip-flop.
  To avoid incorrect operation, we must increase the clock period to allow for the maximum clock skew.

## Slide 33: Asynchronous Inputs
Clocked synchronous circuits
  Inputs, state, and outputs sampled or changed in relation to a common reference signal (called the clock)
Asynchronous circuits
  Inputs, state, and outputs sampled or changed independently of a common reference signal
  Some system inputs must be asynchronous
    reset signal, memory wait, user input
  Unstable states are a major concern
Asynchronous inputs to synchronous circuits
  Because synchronous inputs are greatly preferred, we use a synchronizer

## Slide 34: Synchronizer
Use a synchronizer to translate asynchronous input
  An asynchronous input will remain “asserted” until acknowledged

## Slide 35: Synchronizer
What happens if the asynchronous input is transitioning between 0 and 1?
  The signal is not stable for the required setup and hold times
  The synchronizer may enter a metastable state
  The output will be neither 0 or 1
  This situation is called synchronizer failure

## Slide 36: Synchronization Failure
D
D
Q
Q
asynchronous
input
synchronized
input
synchronous system
Clk
Probability of failure can never be reduced to 0, but it can be reduced:
  slow down the system clock: this gives the synchronizer more time to decay into a steady state; synchronizer failure becomes a big problem for very high speed systems
  use fastest possible logic technology in the synchronizer: this makes for a very sharp "peak" upon which to balance
  cascade two synchronizers: this effectively synchronizes twice (both would have to fail)

## Slide 37: Handling Asynchronous Inputs
D
Q
D
Q
Q0
Clock
Clock
Q1
Async
Input
D
Q
D
Q
Q0
Clock
Clock
Q1
Async
Input
D
Q
Clocked
Synchronous
System
Synchronizer
Never allow asynchronous inputs to fan-out to more than one flip-flop
  Synchronize as soon as possible and then treat as synchronous signal

## Slide 38: Registers
R
S
R
S
R
S
D
Q
D
Q
D
Q
D
Q
OUT1
OUT2
OUT3
OUT4
CLK
IN1
IN2
IN3
IN4
R
S
"0"
Collections of flip-flops with similar controls and logic
  Stored values somehow related (e.g., form binary value)
  Share clock, reset, and set lines
  Similar logic at each stage
Examples
  Shift registers
  Counters

## Slide 39: Shift Register
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK
Holds samples of input
  Store last 4 input values in sequence
  4-bit shift register:

## Slide 40: Universal Shift Register
clear sets the register contents and output to 0 s1 and s0 determine the shift function s0 s1 function 0 0 hold state 0 1 shift right 1 0 shift left 1 1 load new input
left_in
left_out
right_out
clear
right_in
output
input
s0
s1
clock
Holds 4 values
  Serial or parallel inputs
  Serial or parallel outputs
  Permits shift left or right
  Shift in new values from left or right

## Slide 41: Design of Universal Shift Register
Nth cell
s0 and s1 control mux
0
1
2
3
D
Q
CLK
CLEAR
Q[N-1] (left)
Q[N+1] (right)
Input[N]
to N-1th cell
to N+1th cell
clear s0 s1 new value 1 – – 0 0 0 0 output 0 0 1 output value of FF to left (shift right) 0 1 0 output value of FF to right (shift left) 0 1 1 input
Consider one of the four flip-flops
  New value at next clock cycle:

## Slide 42: Pattern Recognizer
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK
OUT
Combinational function of input samples
  In this case, recognizing the pattern 1001 on the single input signal

## Slide 43: Counters
Sequences through a fixed set of patterns
  In this case, 1000, 0100, 0010, 0001
  If one of the patterns is its initial state (by loading or set/reset)
Mobius (or Johnson) counter
  In this case, 1000, 1100, 1110, 1111, 0111, 0011, 0001, 0000
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK

## Slide 44: Register Files
A register file consists of a set of registers that can be read and written by supplying a register number to be accessed.

## Slide 45: Register Files: Read

## Slide 46: Register Files: Write