## Slide 1: CDA 3103
Recitation 10 – Memory

## Slide 7: Data Placement and Identification
Total bits = 32
#bits for block offset = log2(block size) = m
#bits for index = log2(# cache lines) = n
#tag bits = 32 - m - n

## Slide 8: Write Policy
Write through: The information is written to both the block in the cache and to the block in the lower-level memory.
Write back: The information is written only to the block in the cache. The modified cache block is written to main memory only when it is replaced.
  Is block clean or dirty?
Pros and Cons of each:
  WT: read misses do not need to write back evicted line contents
  WB: no writes of repeated writes

## Slide 9: Cache Recap
Caches create an illusion of large amounts of fast memory
Cache Details
  Organization: direct mapped, set associative, fully associative
  Write policy: write-through vs. write-back
  Replacement policy: direct, LRU, random

## Slide 10: Cache Example
Assume we have a 2-way set associative cache, with 16 blocks. Each block is one word in width. Show the result (hit/miss) for the following address access sequence and show the final contents of the cache
2, 3, 11, 16, 21, 13, 11, 3, 22, 4, 5, 11
These are word addresses
  No block offset is needed

## Slide 11: Cache Example
 | Set 0 | Set 1
0 |  | 
1 |  | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Address | Tag | Index | Result
2 |  |  | 
3 |  |  | 
11 |  |  | 
16 |  |  | 
21 |  |  | 
13 |  |  | 
11 |  |  | 
3 |  |  | 
22 |  |  | 
4 |  |  | 
5 |  |  | 
11 |  |  | 

## Slide 12: Cache Example
 | Set 0 | Set 1
0 |  | 
1 |  | 
2 | Mem[2] | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 |  |  | 
11 |  |  | 
16 |  |  | 
21 |  |  | 
13 |  |  | 
11 |  |  | 
3 |  |  | 
22 |  |  | 
4 |  |  | 
5 |  |  | 
11 |  |  | 

## Slide 13: Cache Example
 | Set 0 | Set 1
0 |  | 
1 |  | 
2 | Mem[2] | 
3 | Mem[3] | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 |  |  | 
16 |  |  | 
21 |  |  | 
13 |  |  | 
11 |  |  | 
3 |  |  | 
22 |  |  | 
4 |  |  | 
5 |  |  | 
11 |  |  | 

## Slide 14: Cache Example
 | Set 0 | Set 1
0 |  | 
1 |  | 
2 | Mem[2] | 
3 | Mem[3] | Mem[11]
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 |  |  | 
21 |  |  | 
13 |  |  | 
11 |  |  | 
3 |  |  | 
22 |  |  | 
4 |  |  | 
5 |  |  | 
11 |  |  | 

## Slide 15: Cache Example
 | Set 0 | Set 1
0 | Mem[16] | 
1 |  | 
2 | Mem[2] | 
3 | Mem[3] | Mem[11]
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 | 10 | 000 | Miss
21 |  |  | 
13 |  |  | 
11 |  |  | 
3 |  |  | 
22 |  |  | 
4 |  |  | 
5 |  |  | 
11 |  |  | 

## Slide 16: Cache Example
 | Set 0 | Set 1
0 | Mem[16] | 
1 |  | 
2 | Mem[2] | 
3 | Mem[3] | Mem[11]
4 |  | 
5 | Mem[21] | 
6 |  | 
7 |  | 
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 | 10 | 000 | Miss
21 | 10 | 101 | Miss
13 |  |  | 
11 |  |  | 
3 |  |  | 
22 |  |  | 
4 |  |  | 
5 |  |  | 
11 |  |  | 

## Slide 17: Cache Example
 | Set 0 | Set 1
0 | Mem[16] | 
1 |  | 
2 | Mem[2] | 
3 | Mem[3] | Mem[11]
4 |  | 
5 | Mem[21] | Mem[13]
6 |  | 
7 |  | 
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 | 10 | 000 | Miss
21 | 10 | 101 | Miss
13 | 01 | 101 | Miss
11 |  |  | 
3 |  |  | 
22 |  |  | 
4 |  |  | 
5 |  |  | 
11 |  |  | 

## Slide 18: Cache Example
 | Set 0 | Set 1
0 | Mem[16] | 
1 |  | 
2 | Mem[2] | 
3 | Mem[3] | Mem[11]
4 |  | 
5 | Mem[21] | Mem[13]
6 |  | 
7 |  | 
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 | 10 | 000 | Miss
21 | 10 | 101 | Miss
13 | 01 | 101 | Miss
11 | 01 | 011 | Hit
3 |  |  | 
22 |  |  | 
4 |  |  | 
5 |  |  | 
11 |  |  | 

## Slide 19: Cache Example
 | Set 0 | Set 1
0 | Mem[16] | 
1 |  | 
2 | Mem[2] | 
3 | Mem[3] | Mem[11]
4 |  | 
5 | Mem[21] | Mem[13]
6 |  | 
7 |  | 
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 | 10 | 000 | Miss
21 | 10 | 101 | Miss
13 | 01 | 101 | Miss
11 | 01 | 011 | Hit
3 | 00 | 011 | Hit
22 |  |  | 
4 |  |  | 
5 |  |  | 
11 |  |  | 

## Slide 20: Cache Example
 | Set 0 | Set 1
0 | Mem[16] | 
1 |  | 
2 | Mem[2] | 
3 | Mem[3] | Mem[11]
4 |  | 
5 | Mem[21] | Mem[13]
6 | Mem[22] | 
7 |  | 
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 | 10 | 000 | Miss
21 | 10 | 101 | Miss
13 | 01 | 101 | Miss
11 | 01 | 011 | Hit
3 | 00 | 011 | Hit
22 | 10 | 110 | Miss
4 |  |  | 
5 |  |  | 
11 |  |  | 

## Slide 21: Cache Example
 | Set 0 | Set 1
0 | Mem[16] | 
1 |  | 
2 | Mem[2] | 
3 | Mem[3] | Mem[11]
4 | Mem[4] | 
5 | Mem[21] | Mem[13]
6 | Mem[22] | 
7 |  | 
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 | 10 | 000 | Miss
21 | 10 | 101 | Miss
13 | 01 | 101 | Miss
11 | 01 | 011 | Hit
3 | 00 | 011 | Hit
22 | 10 | 110 | Miss
4 | 00 | 100 | Miss
5 |  |  | 
11 |  |  | 

## Slide 22: Cache Example
 | Set 0 | Set 1
0 | Mem[16] | 
1 |  | 
2 | Mem[2] | 
3 | Mem[3] | Mem[11]
4 | Mem[4] | 
5 | Mem[5] | Mem[13]
6 | Mem[22] | 
7 |  | 
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 | 10 | 000 | Miss
21 | 10 | 101 | Miss
13 | 01 | 101 | Miss
11 | 01 | 011 | Hit
3 | 00 | 011 | Hit
22 | 10 | 110 | Miss
4 | 00 | 100 | Miss
5 | 00 | 101 | Miss
11 |  |  | 

## Slide 23: Cache Example
 | Set 0 | Set 1
0 | Mem[16] | 
1 |  | 
2 | Mem[2] | 
3 | Mem[3] | Mem[11]
4 | Mem[4] | 
5 | Mem[5] | Mem[13]
6 | Mem[22] | 
7 |  | 
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 | 10 | 000 | Miss
21 | 10 | 101 | Miss
13 | 01 | 101 | Miss
11 | 01 | 011 | Hit
3 | 00 | 011 | Hit
22 | 10 | 110 | Miss
4 | 00 | 100 | Miss
5 | 00 | 101 | Miss
11 | 01 | 011 | Hit

## Slide 24: Cache Performance
Suppose we have a system where the instruction cache has a miss rate of 3% and the miss penalty for the data cache is 20 cycles.
Compare the relative performance of our system to one with an ideal cache and one without caching, where memory access requires 35 cycles
Assume a base CPI of 1.

## Slide 25: Cache Performance
Suppose we have a system where the instruction cache has a miss rate of 3% and the miss penalty for the data cache is 20 cycles.
Compare the relative performance of our system to one with an ideal cache and one without caching, where memory access requires 35 cycles.
Assume a base CPI of 1.
With an ideal cache the cpu time is
  IC*CPI*CC
  = IC*1*CC

## Slide 26: Cache Performance
Suppose we have a system where the instruction cache has a miss rate of 3% and the miss penalty for the data cache is 20 cycles.
Compare the relative performance of our system to one with an ideal cache and one without caching, where memory access requires 35 cycles.
Assume a base CPI of 1.
With an ideal cache the cpu time is IC*CC.
With our instruction cache, the effective CPI is (1 + .03*20) = 1.6. The cpu time is IC*CC*1.6

## Slide 27: Cache Performance
Suppose we have a system where the instruction cache has a miss rate of 3% and the miss penalty for the data cache is 20 cycles.
Compare the relative performance of our system to one with an ideal cache and one without caching, where memory access requires 35 cycles.
Assume a base CPI of 1.
With an ideal cache the cpu time is IC*CC.
With our instruction cache, the effective CPI is (1 + .03*20) = 1.6. The cpu time is IC*CC*1.6
Without a cache, the effective CPI is 35. The cpu time is IC*CC*35.

## Slide 28: Cache Performance
Suppose we have a system where the instruction cache has a miss rate of 3% and the miss penalty for the data cache is 20 cycles.
Compare the relative performance of our system to one with an ideal cache and one without caching, where memory access requires 35 cycles.
Assume a base CPI of 1.
With an ideal cache the cpu time is IC*CC.
With our instruction cache, the effective CPI is (1 + .03*20) = 1.6. The cpu time is IC*CC*1.6
Without a cache, the effective CPI is 35. The cpu time is IC*CC*35.
The ideal cache is 1.6 times better than our cache.
Our cache is 21.875 times better than a system without a cache.

## Slide 29: Virtual Memory
The address used by a programmer will be called a logical address
An address in main memory is called a physical address

## Slide 30: Virtual Memory
Only part of the program needs to be in memory for execution
Logical address space can therefore be much larger than physical address space
Allows for more efficient process creation

## Slide 31: Virtual Memory
The term page refers to groups of address space of the same size
For example: if auxiliary memory contains 1024K and main memory contains 32K and page size equals to 1K, then auxiliary memory has 1024 pages and main memory has 32 pages

## Slide 32: Paging
Each process has its own page table
Each page table entry contains the frame number of the corresponding page in main memory
A bit is needed to indicate whether the page is in main memory or not

## Slide 34: Translation Lookaside Buffer
Each virtual memory reference can cause two physical memory accesses
  One to fetch the page table
  One to fetch the data
To overcome this problem a high-speed cache is set up for page table entries
  Called a Translation Lookaside Buffer (TLB)

## Slide 35: Translation Lookaside Buffer
Contains page table entries that have been most recently used
Given a virtual address, processor examines the TLB
If page table entry is present (TLB hit), the frame number is retrieved and the real address is formed
If page table entry is not found in the TLB (TLB miss), the page number is used to index the process page table

## Slide 36: Translation Lookaside Buffer
First checks if page is already in main memory
  If not in main memory a page fault is issued
The TLB is updated to include the new page entry

## Slide 41: Questions?