## Slide 1: Computer Arithmetic

## Slide 2: Background Information
Binary Numbers
  2’s Complement representation
  Addition
  Subtraction
Arithmetic Logic Unit
  Contains Adders to perform addition and subtraction

## Slide 3: Integer Multiplication
“Paper and pencil” example
Multiplicand 1000 Multiplier x 1001 1000 0000 0000 Shift after each step + 1000 Product 01001000

## Slide 4: Observations
Number of bits in the product is larger than the number in either the multiplicand or the multiplier.
  m bits x n bits = m+n bit product
  Overflow is a possible issue
Binary rules – “choices”
  0 => place 0 ( 0 x multiplicand)
  1 => place a copy ( 1 x multiplicand)
3 versions of unsigned multiplication hardware
  successive refinement

## Slide 5: Combinational Multiplier
Partial product accumulation
A0
B0
A0 B0
A1
B1
A1 B0
A0 B1
A2
B2
A2 B0
A1 B1
A0 B2
A3
B3
A2 B0
A2 B1
A1 B2
A0 B3
A3 B1
A2 B2
A1 B3
A3 B2
A2 B3
A3 B3
S6
S5
S4
S3
S2
S1
S0
S7

## Slide 6: Combinational Multiplier
Partial product accumulation
Note use of parallel carry-outs to form higher order sums
12 Adders, if full adders, this is 6 gates each = 72 gates
16 gates form the partial products
total = 88 gates

## Slide 7: Multiplication
Insight from paper and pencil algorithm
  Shift the multiplicand left one digit each step
  With 32 steps in a 32-bit number, we move 32 bits to the left
  Requires a 64-bit register
  Place 32 zeroes in the left half (unoccupied half)
    Unsigned numbers do not require sign extension
  Multiplicand will be added to the sum in the product register
    Product register will also be 64 bits
    Requires a 64 bit ALU to add

## Slide 8: Multiplication Hardware Version 1
64-bit Multiplicand reg, 64-bit ALU, 64-bit Product reg, 32-bit multiplier reg
Figure 4.25 from text

## Slide 9: Multiplication Algorithm Version 1
Done
D
o
n
e
1
.
T
e
s
t
M
u
l
t
i
p
l
i
e
r
0
1
a
.
A
d
d
m
u
l
t
i
p
l
i
c
a
n
d
t
o
p
r
o
d
u
c
t
a
n
d
p
l
a
c
e
t
h
e
r
e
s
u
l
t
i
n
P
r
o
d
u
c
t
r
e
g
i
s
t
e
r
2
.
S
h
i
f
t
t
h
e
M
u
l
t
i
p
l
i
c
a
n
d
r
e
g
i
s
t
e
r
l
e
f
t
1
b
i
t
3
.
S
h
i
f
t
t
h
e
M
u
l
t
i
p
l
i
e
r
r
e
g
i
s
t
e
r
r
i
g
h
t
1
b
i
t
3
2
n
d
r
e
p
e
t
i
t
i
o
n
?
S
t
a
r
t
M
u
l
t
i
p
l
i
e
r
0
=
0
M
u
l
t
i
p
l
i
e
r
0
=
1
N
o
:
<
3
2
r
e
p
e
t
i
t
i
o
n
s
Y
e
s
:
3
2
r
e
p
e
t
i
t
i
o
n
s
Figure 4.26 from text

## Slide 10: Multiplication Example (11x9)
Iter. Step Product Multiplicand Multiplier Action
0 0 00000000 00001011 1001 Initialize
1 1a. 00001011 00001011 1001 Add
1 2,3 00001011 00010110 0100 Shifts
2 1 00001011 00010110 0100 Test-no add
2 2,3 00001011 00101100 0010 Shifts
3 1 00001011 00101100 0010 Test-no add
3 2,3 00001011 01011000 0001 Shifts
4 1a. 01100011 01011000 0001 Add
4 2,3 01100011 1011000 00000 Shifts

## Slide 11: Multiplication is Time Consuming
3 steps per iteration
32 iterations
96 steps total
At 1 clock per step => ~ 100 clocks per multiply

## Slide 12: Observations on Multiplication Version 1
Half the bits of the multiplicand are always 0
  64-bit adder is wasted
0’s inserted in right of multiplicand as shifted
  LSBs of product never changed once formed
Instead of shifting the multiplicand to the left we can shift the product to the right
  Perform some steps in parallel

## Slide 13: Multiplication Hardware Version 2
32-bit Multiplicand reg, 32 -bit ALU, 64-bit Product reg, 32-bit Multiplier reg
Figure 4.28 from text

## Slide 14: Multiplication Algorithm Version 2
Done
Yes: 32 repetitions
D
o
n
e
1
.
T
e
s
t
M
u
l
t
i
p
l
i
e
r
0
1
a
.
A
d
d
m
u
l
t
i
p
l
i
c
a
n
d
t
o
t
h
e
l
e
f
t
h
a
l
f
o
f
t
h
e
p
r
o
d
u
c
t
a
n
d
p
l
a
c
e
t
h
e
r
e
s
u
l
t
i
n
t
h
e
l
e
f
t
h
a
l
f
o
f
t
h
e
P
r
o
d
u
c
t
r
e
g
i
s
t
e
r
2
.
S
h
i
f
t
t
h
e
P
r
o
d
u
c
t
r
e
g
i
s
t
e
r
r
i
g
h
t
1
b
i
t
3
.
S
h
i
f
t
t
h
e
M
u
l
t
i
p
l
i
e
r
r
e
g
i
s
t
e
r
r
i
g
h
t
1
b
i
t
3
2
n
d
r
e
p
e
t
i
t
i
o
n
?
S
t
a
r
t
M
u
l
t
i
p
l
i
e
r
0
=
0
M
u
l
t
i
p
l
i
e
r
0
=
1
N
o
:
<
3
2
r
e
p
e
t
i
t
i
o
n
s
Y
e
s
:
3
2
r
e
p
e
t
i
t
i
o
n
s
Figure 4.29 from text

## Slide 15: Multiplication Example (11x9)
Iter. Step Product Multiplicand Multiplier Action
0 0 00000000 1011 1001 Initialize

## Slide 16: Multiplication Example (11x9)
Iter. Step Product Multiplicand Multiplier Action
0 0 00000000 1011 1001 Initialize
Test the LSB of multiplier
1 indicates Add

## Slide 17: Multiplication Example (11x9)
Iter. Step Product Multiplicand Multiplier Action
0 0 00000000 1011 1001 Initialize
1001 Add
Add the left half of the product to the multiplicand. Store in left half of product.

## Slide 18: Multiplication Example (11x9)
Iter. Step Product Multiplicand Multiplier Action
0 0 00000000 1011 1001 Initialize
1 1a. 1011000 1011 1001 Add
Add the left half of the product to the multiplicand. Store in left half of product.

## Slide 19: Multiplication Example (11x9)
Iter. Step Product Multiplicand Multiplier Action
0 0 00000000 1011 1001 Initialize
1 1a. 1011000 1011 1001 Add
Shift both the product and the multiplier to the right.

## Slide 20: Multiplication Example (11x9)
Iter. Step Product Multiplicand Multiplier Action
0 0 00000000 1011 1001 Initialize
1 1a. 10110000 1011 1001 Add
1 2, 3 01011000 1011 0100 Shifts
Shift both the product and the multiplier to the right.

## Slide 21: Multiplication Example (11x9)
Iter. Step Product Multiplicand Multiplier Action
0 0 00000000 1011 1001 Initialize
1 1a. 10110000 1011 1001 Add
1 2,3 01011000 1011 0100 Shifts
2 1 01011000 1011 0100 Test-no add
2 2,3 00101100 1011 0010 Shifts
3 1 00101100 1011 0010 Test-no add
3 2,3 00010110 1011 0001 Shifts
4 1a. 11000110 1011 0001 Add
4 2,3 01100011 1011 0000 Shifts

## Slide 22: Multiplication Algorithm Version 2
Observation
Product register wastes space (lower half = 0)
  Exactly equal to the size of multiplier left
  We can combine Multiplier register and Product register
Done
Yes: 32 repetitions
D
o
n
e
1
.
T
e
s
t
M
u
l
t
i
p
l
i
e
r
0
1
a
.
A
d
d
m
u
l
t
i
p
l
i
c
a
n
d
t
o
t
h
e
l
e
f
t
h
a
l
f
o
f
t
h
e
p
r
o
d
u
c
t
a
n
d
p
l
a
c
e
t
h
e
r
e
s
u
l
t
i
n
t
h
e
l
e
f
t
h
a
l
f
o
f
t
h
e
P
r
o
d
u
c
t
r
e
g
i
s
t
e
r
2
.
S
h
i
f
t
t
h
e
P
r
o
d
u
c
t
r
e
g
i
s
t
e
r
r
i
g
h
t
1
b
i
t
3
.
S
h
i
f
t
t
h
e
M
u
l
t
i
p
l
i
e
r
r
e
g
i
s
t
e
r
r
i
g
h
t
1
b
i
t
3
2
n
d
r
e
p
e
t
i
t
i
o
n
?
S
t
a
r
t
M
u
l
t
i
p
l
i
e
r
0
=
0
M
u
l
t
i
p
l
i
e
r
0
=
1
N
o
:
<
3
2
r
e
p
e
t
i
t
i
o
n
s
Y
e
s
:
3
2
r
e
p
e
t
i
t
i
o
n
s
Figure 4.29 from text

## Slide 23: Multiplication Hardware Version 3
32-bit Multiplicand reg, 32-bit ALU, 64-bit Product reg, (no Multiplier reg)
Figure 4.31 from text

## Slide 24: Multiplication Algorithm Version 3
Done
D
o
n
e
1
.
T
e
s
t
P
r
o
d
u
c
t
0
1
a
.
A
d
d
m
u
l
t
i
p
l
i
c
a
n
d
t
o
t
h
e
l
e
f
t
h
a
l
f
o
f
t
h
e
p
r
o
d
u
c
t
a
n
d
p
l
a
c
e
t
h
e
r
e
s
u
l
t
i
n
t
h
e
l
e
f
t
h
a
l
f
o
f
t
h
e
P
r
o
d
u
c
t
r
e
g
i
s
t
e
r
2
.
S
h
i
f
t
t
h
e
P
r
o
d
u
c
t
r
e
g
i
s
t
e
r
r
i
g
h
t
1
b
i
t
3
2
n
d
r
e
p
e
t
i
t
i
o
n
?
S
t
a
r
t
P
r
o
d
u
c
t
0
=
0
P
r
o
d
u
c
t
0
=
1
N
o
:
<
3
2
r
e
p
e
t
i
t
i
o
n
s
Y
e
s
:
3
2
r
e
p
e
t
i
t
i
o
n
s
Figure 4.32 from text

## Slide 25: Multiplication Example (11x9)
Iter. Step Product Multiplicand Action
0 0 0000 1001 1011 Initialize
1 1a. 1011 1001 1011 Add
1 2 0101 1100 1011 Shift
2 1 0101 1100 1011 Test-no add
2 2 0010 1110 1011 Shift
3 1 0010 1110 1011 Test-no add
3 2 0001 0111 1011 Shift
4 1a. 1100 0111 1011 Add
4 2 0110 0011 1011 Shift
Note: Multiplier in Product Register is underlined

## Slide 26: Multiplying by a Constant
Some compilers replace multiplies by short constants with a series of shifts and adds. Because one bit to the left represents a number twice as large in base 2, shifting the bits left has the same effect as multiplying by a power of 2.
Almost every compiler will perform the strength reduction optimization of substituting a left shift for a multiply by a power of 2.

## Slide 27: Multiplying by a Constant
Some compilers replace multiplies by short constants with a series of shifts and adds. Because one bit to the left represents a number twice as large in base 2, shifting the bits left has the same effect as multiplying by a power of 2.
Almost every compiler will perform the strength reduction optimization of substituting a left shift for a multiply by a power of 2.
4 * 2 = 8
0100 * 0010 = 1000
0100 << 1 = 1000

## Slide 28: Multiplying by a Constant
Some compilers replace multiplies by short constants with a series of shifts and adds. Because one bit to the left represents a number twice as large in base 2, shifting the bits left has the same effect as multiplying by a power of 2.
Almost every compiler will perform the strength reduction optimization of substituting a left shift for a multiply by a power of 2.
2 * 4 = 8
0010 * 0100 = 1000
0010 << 2 = 1000

## Slide 29: Signed Multiplication
So far, we have multiplied unsigned numbers
What about signed multiplication?
  one solution: make both positive
  leave out the sign bit, run for 31 steps
  set sign bit negative if signs of inputs differ

## Slide 30: Booth’s Algorithm
multiply two’s complement signed numbers
uses same hardware as before
can also be used to reduce the number of steps

## Slide 31: Insight for Booth’s Algorithm
Example: 2 x 6 = 0010 x 0110:
0010 x 0110 + 0000 shift (0 in multiplier) + 0010 add (1 in multiplier) + 0010 add (1 in multiplier) + 0000 shift (0 in multiplier) 00001100
ALU can get same result in more than one way:
  6 x = 4x + 2x or 6x = – 2x + 8 x
  111 = 1000 – 0001
  1111 = 10000 – 00001
  1111XXX = 10000XXX – 00001XXX

## Slide 32: Insight for Booth’s Algorithm
Replace string of 1s in multiplier with
  initially subtract when we see first 1 (from right)
  later, add when we see 0 at left end of the string of 1s.
Example
0010 x 0110 + 0000 shift (0 in multiplier) - 0010 subtract (first 1 in string) + 0000 shift (within string of 1s) + 0010 add (end of string) 00001100
Effectively: 2 x 6 = 2 x 8 – 2 x 2

## Slide 33: Booth’s Algorithm
Current Right Explanation Example
1 0 Beginning of a run of 1s 0001111000
1 1 Middle of a run of 1s 0001111000
0 1 End of a run of 1s 0001111000
0 0 Middle of a run of 0s 0001111000

## Slide 34: Booth’s Algorithm
Depending on the current and previous bits, do one of the following: 00: Middle of a string of 0s, so no arithmetic operations. 01: End of a string of 1s, so add the multiplicand to the left half of the product. 10: Beginning of a string of 1s, so subtract the multiplicand from the left half of the product. 11: Middle of a string of 1s, so no arithmetic operation.
As in the previous algorithm, shift the Product register right (arithmetic shift) 1 bit.
Notes: 0. 0010 x 0000 0110 0
1a. 00 nop: 0000 0110 0
2. Shr: 0000 0011 0 (2 x 3)
1c: 10 Pr-M 1110 0011 0
2. Shr: 1111 0001 1
1d. 11 nop 1111 0001 1
2. Shr: 1111 1000 1
1b: 01 PR+M 0001 1000 1
2. Shr: 0000 1100 0
0. 0010 x 0000 1101 0 (2 x -3)
1c: 10 Pr-M : 1110 1101 0
2. Shr: 1111 0110 1
1b: 01 PR+M 0001 0110 1
2. Shr: 0000 1011 0
1c: 10 Pr-M : 1110 1011 0
2. Shr: 1111 0101 1
1d. 11 nop 1111 0101 1
2. Shr: 1111 1010 1

## Slide 35: Booth’s Example (-5 x -6)
Multiplicand = –6 = 1010; –Multiplicand = 6 = 0110
Multiplier = –5 = 1011
Iter. Step Product Last Action
0 0 0000 101(1 0) 0 Initialize
1 1.10 0110 101(1 0) 0 Start string: Subtract => Add 0110
1 2 0011 010(1 1) 1 Shift arithmetic
2 1.11 0011 010(1 1) 1 Middle string: nothing
2 2 0001 101(0 1) 1 Shift arithmetic
3 1.01 1011 101(0 1) 1 End string: add 1010
3 2 1101 110(1 0) 0 Shift arithmetic
4 1.10 0011 110(1 0) 0 Start string: Subtract => add 0110
4 2 0001 1110 0 Shift arithmetic
Notes: 1. Multiplier in Product Register is underlined. 2. Current/previous bits are in parentheses.
3. Previous bit is initialized to 0

## Slide 36: Booth’s Algorithm
Originally for speed: Shifts are faster than add
Key advantage today: Works properly for 2’s complement numbers without requiring special fix for sign!

## Slide 37: Division: Paper and Pencil
“Paper and pencil” example
20 ÷ 6 = 3 Remainder 2
    00011 Quotient
    110 10100 Dividend 10 101 1010 - 110_
    1000
    - 110
    10 Remainder
Divisor

## Slide 38: Division: Paper and Pencil
“Paper and pencil” example
20 ÷ 6 = 3 Remainder 2
    00011 Quotient
    110 10100 Dividend 10 101 1010 - 110_
    1000
    - 110
    10 Remainder
    Dividend = Quotient * Divisor + Remainder
Divisor

## Slide 39: Division: Paper and Pencil
“Paper and pencil” example
20 ÷ 6 = 3 Remainder 2
    00011 Quotient
    110 10100 Dividend 10 101 1010 - 110_
    1000
    - 110
    10 Remainder
Divisor
Algorithm: If Partial Remainder > Divisor then Quotient bit = 1; Remainder = Remainder – Divisor
else Quotient bit = 0 Shift down next dividend bit

## Slide 40: Division Algorithm
If the partial remainder > divisor (The divisor goes into the portion of the dividend 1 time) then Quotient bit = 1; Remainder = Remainder – Divisor
else (The divisor does not go into the portion of the dividend)
Quotient bit = 0
Shift down next dividend bit

## Slide 41: Division Hardware Version 1
64-bit Divisor reg (divisor in upper half), 64-bit ALU, 64-bit Remainder reg (dividend in lower half), 32-bit Quotient reg.
6
4
-
b
i
t
A
L
U
C
o
n
t
r
o
l
t
e
s
t
Q
u
o
t
i
e
n
t
S
h
i
f
t
l
e
f
t
R
e
m
a
i
n
d
e
r
W
r
i
t
e
D
i
v
i
s
o
r
S
h
i
f
t
r
i
g
h
t
6
4
b
i
t
s
6
4
b
i
t
s
3
2
b
i
t
s
Figure 4.36 from text

## Slide 42: Division Algorithm Version 1
Takes n+1 Steps for n-bit Quotient and Remainder
2a. Quotient = Quotient <<1;
Quotient ++;
Done
Start
D
o
n
e
T
e
s
t
R
e
m
a
i
n
d
e
r
2
a
.
S
h
i
f
t
t
h
e
Q
u
o
t
i
e
n
t
r
e
g
i
s
t
e
r
t
o
t
h
e
l
e
f
t
,
s
e
t
t
i
n
g
t
h
e
n
e
w
r
i
g
h
t
m
o
s
t
b
i
t
t
o
1
3
.
S
h
i
f
t
t
h
e
D
i
v
i
s
o
r
r
e
g
i
s
t
e
r
r
i
g
h
t
1
b
i
t
3
3
r
d
r
e
p
e
t
i
t
i
o
n
?
S
t
a
r
t
R
e
m
a
i
n
d
e
r
<
0
N
o
:
<
3
3
r
e
p
e
t
i
t
i
o
n
s
Y
e
s
:
3
3
r
e
p
e
t
i
t
i
o
n
s
2
b
.
R
e
s
t
o
r
e
t
h
e
o
r
i
g
i
n
a
l
v
a
l
u
e
b
y
a
d
d
i
n
g
t
h
e
D
i
v
i
s
o
r
r
e
g
i
s
t
e
r
t
o
t
h
e
R
e
m
a
i
n
d
e
r
r
e
g
i
s
t
e
r
a
n
d
p
l
a
c
e
t
h
e
s
u
m
i
n
t
h
e
R
e
m
a
i
n
d
e
r
r
e
g
i
s
t
e
r
.
A
l
s
o
s
h
i
f
t
t
h
e
Q
u
o
t
i
e
n
t
r
e
g
i
s
t
e
r
t
o
t
h
e
l
e
f
t
,
s
e
t
t
i
n
g
t
h
e
n
e
w
l
e
a
s
t
s
i
g
n
i
f
i
c
a
n
t
b
i
t
t
o
0
1
.
S
u
b
t
r
a
c
t
t
h
e
D
i
v
i
s
o
r
r
e
g
i
s
t
e
r
f
r
o
m
t
h
e
R
e
m
a
i
n
d
e
r
r
e
g
i
s
t
e
r
a
n
d
p
l
a
c
e
t
h
e
r
e
s
u
l
t
i
n
t
h
e
R
e
m
a
i
n
d
e
r
r
e
g
i
s
t
e
r
R
e
m
a
i
n
d
e
r
>
0
–
Figure 4.37 from text

## Slide 43: Division Example
Example: 7÷3 = 2; remainder 1.
Iter Step Remainder Divisor Quotient Action
0 0 000111 011000 000 Initialize
1 1 101111 011000 000 Subtract
1 2b. 000111 011000 000 Restore; shift
1 3 000111 001100 000 Shift divisor
2 1 111010 001100 000 Subtract
2 2b. 000111 001100 000 Restore; shift
2 3 000111 000110 000 Shift divisor
3 1 000001 000110 000 Subtract
3 2a. 000001 000110 001 Shift in 1
3 3 000001 000011 001 Shift divisor
4 1 111110 000011 001 Subtract
4 2b. 000001 000011 010 Restore; shift
4 3 000001 000001 010 Shift divisor

## Slide 44: Observations on Division Version 1
Half the bits in divisor always 0
  Half of 64-bit adder is wasted
  Half of divisor is wasted
Instead of shifting the divisor right, we can shift the remainder left
The first step cannot produce a 1 in quotient bit (otherwise the quotient will be too big)
  switch order to shift first and then subtract, saves 1 iteration

## Slide 45: Division Hardware Version 2
32-bit Divisor register, 32 -bit ALU, 64-bit Remainder register, 32-bit Quotient register
C
o
n
t
r
o
l
t
e
s
t
Q
u
o
t
i
e
n
t
S
h
i
f
t
l
e
f
t
W
r
i
t
e
3
2
b
i
t
s
6
4
b
i
t
s
3
2
b
i
t
s
S
h
i
f
t
l
e
f
t
D
i
v
i
s
o
r
3
2
-
b
i
t
A
L
U
R
e
m
a
i
n
d
e
r
Figure 4.39 from text

## Slide 46: Division Algorithm Version 2
2a. Quotient = Quotient <<1;
Quotient ++;
Done
1. Remainder = Remainder – Divisor
Test
Remainder
Remainder < 0
Remainder >= 0
3. Remainder = Remainder << 1
32
repetitions?
No
Yes
Start
0. Remainder = Dividend << 1;
2b. Remainder = Remainder + Divisor;
Quotient <<1;
Takes n Steps for n-bit Quotient and Remainder
Affects Upper
Half of Remainder

## Slide 47: Observations on Division Version 2
Remainder register loses a bit every cycle; quotient gains a bit every cycle.
We can eliminate the Quotient register by combining it with the Remainder register
  Shift both to the left in one statement (by shifting the Remainder left as before and putting quotient in LSBs).
  Loop contains only two steps:
    subtract
    restore/leave and shift
  Consequence of combining two registers and new order of operations in loop:
    remainder shifted left one time too many.
  Final correction step must shift back remainder in the left half of the register.

## Slide 48: Division Hardware Version 3
32-bit Divisor reg, 32 -bit ALU, 64-bit Remainder reg, (0-bit Quotient reg)
W
r
i
t
e
3
2
b
i
t
s
6
4
b
i
t
s
S
h
i
f
t
l
e
f
t
S
h
i
f
t
r
i
g
h
t
R
e
m
a
i
n
d
e
r
3
2
-
b
i
t
A
L
U
D
i
v
i
s
o
r
C
o
n
t
r
o
l
t
e
s
t
Figure 4.41 from text

## Slide 49: Division Algorithm Version 3
Start
D
o
n
e
.
S
h
i
f
t
l
e
f
t
h
a
l
f
o
f
R
e
m
a
i
n
d
e
r
r
i
g
h
t
1
b
i
t
T
e
s
t
R
e
m
a
i
n
d
e
r
3
a
.
S
h
i
f
t
t
h
e
R
e
m
a
i
n
d
e
r
r
e
g
i
s
t
e
r
t
o
t
h
e
l
e
f
t
,
s
e
t
t
i
n
g
t
h
e
n
e
w
r
i
g
h
t
m
o
s
t
b
i
t
t
o
1
3
2
n
d
r
e
p
e
t
i
t
i
o
n
?
S
t
a
r
t
R
e
m
a
i
n
d
e
r
<
0
N
o
:
<
3
2
r
e
p
e
t
i
t
i
o
n
s
Y
e
s
:
3
2
r
e
p
e
t
i
t
i
o
n
s
3
b
.
R
e
s
t
o
r
e
t
h
e
o
r
i
g
i
n
a
l
v
a
l
u
e
b
y
a
d
d
i
n
g
t
h
e
D
i
v
i
s
o
r
r
e
g
i
s
t
e
r
t
o
t
h
e
l
e
f
t
h
a
l
f
o
f
t
h
e
R
e
m
a
i
n
d
e
r
r
e
g
i
s
t
e
r
a
n
d
p
l
a
c
e
t
h
e
s
u
m
i
n
t
h
e
l
e
f
t
h
a
l
f
o
f
t
h
e
R
e
m
a
i
n
d
e
r
r
e
g
i
s
t
e
r
.
A
l
s
o
s
h
i
f
t
t
h
e
R
e
m
a
i
n
d
e
r
r
e
g
i
s
t
e
r
t
o
t
h
e
l
e
f
t
,
s
e
t
t
i
n
g
t
h
e
n
e
w
r
i
g
h
t
m
o
s
t
b
i
t
t
o
0
2
.
S
u
b
t
r
a
c
t
t
h
e
D
i
v
i
s
o
r
r
e
g
i
s
t
e
r
f
r
o
m
t
h
e
l
e
f
t
h
a
l
f
o
f
t
h
e
R
e
m
a
i
n
d
e
r
r
e
g
i
s
t
e
r
a
n
d
p
l
a
c
e
t
h
e
r
e
s
u
l
t
i
n
t
h
e
l
e
f
t
h
a
l
f
o
f
t
h
e
R
e
m
a
i
n
d
e
r
r
e
g
i
s
t
e
r
R
e
m
a
i
n
d
e
r
0
1
.
S
h
i
f
t
t
h
e
R
e
m
a
i
n
d
e
r
r
e
g
i
s
t
e
r
l
e
f
t
1
b
i
t
–
>
Figure 4.40 from text
Affects Upper
Half of Remainder
Affects Upper
Half of Remainder
Takes n Steps for n-bit Quotient and Remainder

## Slide 50: Another Divide Example
Example: 14 ÷ 3 = 4; remainder 2.
Iter Step Remainder Divisor Action
0 0 0001 1100 0011 Initialize
1 1 1110 1100 0011 Subtract: Remainder<0
1 2b. 0011 1000 0011 Restore; shift in 0
2 1 0000 1000 0011 Subtract; Remainder=0
2 2a. 0001 0001 0011 Shift in a 1
3 1 1101 0001 0011 Subtract: Remainder<0
3 2b. 0010 0010 0011 Restore; shift in 0
4 1 1110 0010 0011 Subtract: Remainder<0
4 2b. 0100 0100 0011 Restore; shift
3 0010 0100 0011 Shift remainder right
Rem. Quot.

## Slide 51: Observations on Divide Version 3
Same Hardware as Multiply: just need ALU to add or subtract, and 64-bit register to shift left or shift right
Hi and Lo registers in MIPS combine to act as 64-bit register for multiply and divide

## Slide 52: Signed Division
Store the signs of the divisor and dividend
Convert divisor and dividend to positive
Complement quotient and remainder if necessary
  Dividend and Remainder are defined to have same sign
  Quotient negated if Divisor sign and Dividend sign disagree

## Slide 53: Beyond Integers
Real numbers
  Called “float” values
Computer arithmetic that supports real numbers is called floating point arithmetic

## Slide 54: Exponential Notation
The following are equivalent representations of 1,234
The representations differ in that the decimal place – the “point” -- “floats” to the left or right (with the appropriate adjustment in the exponent).
123,400.0 x 10-2
12,340.0 x 10-1
1,234.0 x 100
123.4 x 101
12.34 x 102
1.234 x 103
0.1234 x 104

## Slide 55: Normalized Scientific Notation
A number in scientific notation that has no leading 0s is called a normalized number.
  1.0ten * 10–9 is in normalized scientific notation
  0.1ten * 10–8 is not normalized
  10.0ten * 10–10 is not in scientific notation

## Slide 56: Floating Point: Scientific Notation
Number represented as
  Mantissa
  Radix (base)
  Exponent
In a binary number, the radix (or base) is 2 instead of 10. The general form could be written as 1.xxxxxx * 2yyyyy.
6.02 x 10
23
exponent
radix (base)
Mantissa
decimal point
Sign
magnitude
Sign
magnitude
Notes: To date we have only considered integers
Need a way to adjust position of the binary point: Floating point numbers

## Slide 57: Standards
Floats are implemented using the IEEE 754 standard
  found in virtually every computer invented since 1980
  has greatly improved both the ease of porting floating-point programs and the quality of computer arithmetic.

## Slide 58: Standards
IEEE 754 offers three advantages:
  Simplifies exchange of data that includes floating-point numbers
  Simplifies the floating-point arithmetic algorithms to know that numbers will always be in this form
  Increases the accuracy of the numbers that can be stored, since the unnecessary leading 0s are replaced by real digits

## Slide 59: IEEE 754 Standard
Single precision: 32 bits, consisting of...
  Sign bit (1 bit)
  Exponent (8 bits)
  Mantissa (23 bits)

## Slide 60: IEEE 754 Standard
Single precision: 32 bits, consisting of...
  Sign bit (1 bit)
  Exponent (8 bits)
  Mantissa (23 bits)
Fractions almost as small as 2.0ten * 10–38
Numbers almost as large as 2.0ten * 1038

## Slide 61: IEEE 754 Standard
Single precision: 32 bits, consisting of...
  Sign bit (1 bit)
  Exponent (8 bits)
  Mantissa (23 bits)
Fractions almost as small as 2.0ten * 10–38
Numbers almost as large as 2.0ten * 1038
Overflow may still occur
  Exponent is too large to be represented
Underflow may occur
  Exponent is too small to be represented

## Slide 62: IEEE 754 Standard
Single precision: 32 bits, consisting of...
  Sign bit (1 bit)
  Exponent (8 bits)
  Mantissa (23 bits)
Double precision: 64 bits, consisting of…
  Sign bit (1 bit)
  Exponent (11 bits)
  Mantissa (52 bits)

## Slide 63: Normalization
The mantissa is normalized
Has an implied decimal place on left
Has an implied “1” on left of the decimal place
E.g.,
  Mantissa  10100000000000000000000
  Represents  1.1012 = 1.62510

## Slide 64: Single Precision with Normalization
sign
1
8
23
exponent
fraction
Normalized binary significand with hidden bit (1): 1.M
S
E
M

## Slide 65: Double Precision with Normalization
sign
1
11
52
exponent
fraction
Normalized binary significand with hidden bit (1): 1.M
S
E
M

## Slide 66: Normalization
General form for floating-point numbers: (–1)S * (1+F) * 2E
How do we represent zero?
  E = 0
  F = 0

## Slide 67: Excess Notation
To include positive (+ve) and negative (–ve) exponents, “excess” notation is used
Also called biased notation
Represents the most negative exponent as 0...0two and the most positive exponent as 1…1two.

## Slide 68: Excess Notation
The value of the exponent stored is larger than the actual exponent
Single precision: excess 127
Double precision: excess 1023
Each real number is (–1)S * (1 + Fraction) * 2(Exponent – Bias)
E.g., excess 127,
  Exponent 
  Represents…
10000111
135 – 127 = 8

## Slide 69: Example
Single precision
0 10000010 11000000000000000000000
1.112
130 – 127 = 3
0 = positive mantissa
+1.112 x 23 = 1110.02 = 14.010

## Slide 70: Converting from Floating Point
What decimal value is represented by the following 32-bit floating point number?
1100 0001 0111 1011 0000 0000 0000 00002

## Slide 71: Converting from Floating Point
Step 1: find S, E, and M
1 10000010 111101100000000000000002
S
E
M
1 = negative
0 = positive

## Slide 72: Converting from Floating Point
Step 2: Find “real” exponent, n
  n = E – 127
    = 100000102 – 127
    = 130 – 127
  = 3

## Slide 73: Converting from Floating Point
Step 3: Put S, M, and n together to form binary result
  Don’t forget the implied “1.” on the left of the mantissa.
-1.11110112 x 2n =
-1.11110112 x 23 =
-1111.10112

## Slide 74: Converting from Floating Point
Step 4: Express result in decimal
-1111.10112
-15
2-1 = 0.5
2-3 = 0.125
2-4 = 0.0625
0.6875
Answer: -15.6875

## Slide 75: Converting to Floating Point
Express 36.562510 as a 32-bit floating point number

## Slide 76: Converting to Floating Point
Step 1: Express original value in binary
36.562510 = 100100.10012

## Slide 77: Converting to Floating Point
Step 2: Normalize
100100.10012 = 1.0010010012 x 25

## Slide 78: Converting to Floating Point
Step 3: Determine S, E, and M
+1.0010010012 x 25
S = 0 (because the value is positive)
M
S
n
E = n + 127
= 5 + 127
= 132
= 100001002

## Slide 79: Converting to Floating Point
Step 4: Put S, E, and M together to form 32-bit binary result
0 10000100 001001001000000000000002
S
E
M

## Slide 80: Special Values
Single Precision: Exponents of 0 and 255 have special meaning
  E=0, M=0 represents 0 (sign bit still used so there is +/-0)
  E=0, M≠0 is a denormalised number (+/-0.Mx2-126) (smaller than the smallest normalised number)
  E=255, M=0 represents +/- infinity
  E=255, M ≠ 0 represents NaN (not a number, e.g., returned for 0/0 or sqrt(-1))
Exponent Significand Value
0 0 0
0 nonzero denormalized number
1..emax-1 anything normal floating point number
emax 0 infinity
emax nonzero Not a Number (NaN)

## Slide 81: Denormalized Numbers
Description exp frac
Smallest Possible 00…00 00…01
Denormalized Number
  Single  1.4 X 10–45
  Double  4.9 X 10–324
Largest Possible 00…00 11…11
Denormalized Number
  Single  1.18 X 10–38
  Double  2.2 X 10–308

## Slide 82: Floating Point Operations
Arithmetic:
  multiplication, division:
    multiply/divide mantissa
    add/subtract exponent
    example: 5.6x1011 x 6.7x1012 = 5.6 x 6.7 x 1023
  Addition, subtraction
    convert operands to have the same exponent value
    add/subtract mantissas
    example: 2.1x103 + 4.3x104 = 0.21 x 104 + 4.3 x 104

## Slide 83: Basic Addition Algorithm
Align binary points (denormalize smaller number)
    compute Diff = Exp(Y) – Exp (X);
    Sig(X) = Sig(X) >> Diff
    Exp = Exp(Y)
Add the aligned components
    Sig = Sig (x) + Sig (Y)
Normalize the sum
    Shift Sig right/left until leading bit is 1; decrementing or incrementing Exp.
    Check for overflow in Exp
    Round (needs more bits, as we will see)
    repeat step 3 if not still normalized

## Slide 84: Basic Addition Algorithm

## Slide 85: Addition Example
11 + 6, 4-bit significand
1.0110 x 23 + 1.1000 x 22
Align binary points (denormalize smaller number)
      1.0110 x 23
      +0.1100 x 23
Add the aligned components
      10.0010 x 23 (=17)
Normalize the sum
      1.0001 x 24
  No overflow, no rounding

## Slide 86: Another Addition Example
8.5 – 3.75 = 4.75, 4-bit significand
1.0001x23 – 1.1110x21
Align binary point:
  1.0001 x 23
  -0.0111 x 23
Subtract the aligned components:
  0.1001 x 23 (=4.75)
Normalize:
  1.0010 x 22
  Note our answer is actually 4.5. With only 4-bits we are losing accuracy. Our result would be off by 0.25 or a whole bit in the least significant place.

## Slide 87: Basic Multiplication Algorithm
Compute exponents
  Multiplication: Exp = Exp (X) + Exp (Y) – bias;
  Division: Exp = Exp (X) – Exp(Y) + bias;
Multiply/Divide significands
  Multiplication: Sig = Sig (X) x Sig (Y);
  Division: Sig = Sig(X) / Sig(Y);
Normalize the product
  Shift Sig right until leading bit is 1; incrementing Exp.
  Check for overflow in Exp
  repeat step 3 if not still normalized
Round
  Any bits that do not fit must be discarded
Set sign
  positive if signs same; negative if signs differ

## Slide 88: Basic Multiplication Algorithm

## Slide 89: Multiplication Example
.5 * -.4375, 4-bit significand
1.000two * 2–1 * – 1.110two * 2–2
Compute exponents
-1 + (-2) = -3
Multiply/Divide significands
01110000
Normalize the product
1.110000 * 2–3
Round
1.1100 * 2–3
Set sign
-1.1100 * 2–3 because original signs differ

## Slide 90: Accuracy and Rounding
Floating-point numbers are approximations for a number they can’t really represent.
  Infinite possible real numbers between 0 and 1
  We can only represent 253 of them
  Approximate by rounding

## Slide 91: Rounding Modes
IEEE Standard has four rounding modes:
  round to nearest even (default)
  round towards plus infinity
  round towards minus infinity
  round towards 0
It can be shown that round to nearest even minimizes the mean error introduced by rounding

## Slide 92: Accuracy and Rounding
To round accurately, we need the hardware to include extra bits for the calculation.
Specifically, we keep 2 extra bits on the right
  Guard bit
  Round bit

## Slide 93: Guard Bit
The first bit to the right: an additional digit (bit) used in intermediate calculations to prevent loss of accuracy.

## Slide 94: Examples for Guard Bit
Assume 4-bit significand
Addition: 1.0000 x 20 + 1.1111 x 2–2
1.0000 x 20
+ 0.01111 x 20
1.01111 rounds to 1.1000–right! g 1.0111–would be wrong!
Multiplication:
1.1000 x 20
x 1.1001 x 2–2
10.10110 x 2–2
normalize 1.010110x2-1 round 1.0110x2-1
g

## Slide 95: Round Bit
Bit to the right of guard bit needed for accurate rounding.

## Slide 96: Example for Round Bit
Example: 1.0000 x 20 - 1.0001 x 2–2
  guard and round bits shown
1.0000 x 20
- 0.010001 x 20
0.101111 x 20 Result
1.01111 x 2-1 Normalize
1.1000 x 2-1 Round; simple round up
  Without round bit, result is 1.0111

## Slide 97: Example for Round Bit (base 10)
2.56ten * 100 + 2.34ten * 102, 3 significant decimal digits
.0256 * 102 + 2.34 * 102
2.3656 * 102
Guard digit is 5
Round digit is 6
2.37 * 102
Without additional bits: 2.36 * 102

## Slide 98: Sticky Bit
Round to even problems
  need to know if the answer is exactly even or not.
  With 4-bit significand, if result is 1000X result rounds to 1.0000 if X=0 and 1.0001 otherwise
  Potentially need 2x number of bits
Instead keep “sticky” bit (S):
  used to determine whether there are any 1 bits truncated below the guard and round bits
  S=1 if any bits are off to the right, otherwise S=0

## Slide 99: Example for Sticky Bit
1.0000 x 20 + 1.0001 x 2–5
  guard, round, and sticky bits shown
1.0000 x 20
+ 0.000010 x 20 1
1.000010 x 20 1 Result
1.0001 x 2-0 Round to nearest even Without S rounds to 1.0000.

## Slide 100: Exceptions
Invalid operation
  result of operation is a NaN (except = or !=)
  inf. +/- inf.; 0 * inf; 0/0; inf./inf.; x remainder y, y = 0;
  sqrt(x) where x < 0, x = +/- inf.
Overflow
  result of operation is larger than largest representable number
  flushed to +/- inf. if overflow exception is not enabled

## Slide 101: Exceptions
Divide by 0
  x/0 where x = 0, +/- inf.;
  flushed to +/- inf. if divide by zero exception not enabled
Underflow
  subnormal result OR non-zero result underflows to 0
Inexact
  rounded result not the actual result (rounding error = 0)

## Slide 102: Exceptions
IEEE Standard specifies defaults and allows traps to permit exceptions to be handled at the program level
  contrast with the more usual result of aborting the computation altogether.