## Slide 1: Memory
Memory Hierarchy: Caches

## Slide 2: Introduction
An ideal computing system has unlimited fast memory
  Obviously, this is not possible
  A memory hierarchy gives the illusion of large amounts of fast memory

## Slide 3: Principle of Locality
Programs access only a small proportion of their address space at any time
Temporal locality
  Items accessed recently are likely to be accessed again soon
  e.g., instructions in a loop, induction variables
Spatial locality
  Items near those accessed recently are likely to be accessed soon
  E.g., sequential instruction access, array data

## Slide 4: Memory Technology
Static RAM (SRAM)
  0.5ns – 2.5ns, $2000 – $5000 per GB
Dynamic RAM (DRAM)
  50ns – 70ns, $20 – $75 per GB
Magnetic disk
  5ms – 20ms, $0.20 – $2 per GB

## Slide 5: Memory Hierarchy
Smaller, faster memory is closer to the processor

## Slide 6: Caches
Permanent storage on disk
Copy recently accessed and nearby items from disk to smaller DRAM memory
  Main memory
Copy recently accessed and nearby items from DRAM to smaller SRAM memory
  Cache memory attached to CPU
  Cache may also refer to any storage that takes advantage of locality

## Slide 7: Memory Hierarchy Levels
Block: unit of copying
  May be multiple words
If accessed data is present in upper level
  Hit: access satisfied by upper level
    Hit ratio: hits/accesses
If accessed data is absent
  Miss: block copied from lower level
    Time taken: miss penalty
    Miss ratio: misses/accesses = 1 – hit ratio
  Then accessed data supplied from upper level

## Slide 8: Performance
The time to service hits and misses affects the CPU time.
  Hit time
    time required to access the cache
    includes time to determine if it’s a hit or a miss
  Miss penalty
    time required to fetch a block from the next lowest level
  Hit time < Miss penalty

## Slide 9: Cache Memory
Cache memory
  The level of the memory hierarchy closest to the CPU
Given accesses X1, …, Xn–1, Xn
How do we know if the data is present?
Where do we look?

## Slide 10: Direct Mapped Cache
Each word can go in exactly one place in the cache
  Assign a location based on the address of the word
  (Block address) modulo (#Blocks in cache)

## Slide 11: Direct Mapped Cache
Each word can go in exactly one place in the cache
  Assign a location based on the address of the word
  (Block address) modulo (#Blocks in cache)

## Slide 12: Direct Mapped Cache
Each word can go in exactly one place in the cache
  Assign a location based on the address of the word
  (Block address) modulo (#Blocks in cache)
#Blocks is a power of 2
Use low-order address bits

## Slide 13: Tags and Valid Bits
How do we know which particular block is stored in a cache location?
  Store block address as well as the data
  Only need the high-order bits
  Called the tag
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0

## Slide 14: Cache Read
Reads are simpler because reads do not change the contents of the cache
Example:
  8-Block, Direct Mapped Cache
  Addresses:
  Binary Decimal Cache Block (address mod 8)
  10110 22 110
  11010 26 010
  10110 22 110
  11010 26 010
  10000 16 000
  00011 3 011
  10000 16 000
  10010 18 010
  10000 16 000

## Slide 15: Cache Example
Initial state
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 

## Slide 16: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110

## Slide 17: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010

## Slide 18: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010

## Slide 19: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000

## Slide 20: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 10 | Mem[10010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | 010

## Slide 21: Address Subdivision

## Slide 22: Cache Hit
Index of the address specifies cache block
If the valid bit indicates data is present, check the tags
If the tags match, it is a hit
We can use the data stored in the cache
CPU proceeds normally

## Slide 23: Cache Misses
If the valid bit is not set or if the tags do not match, it is a miss
Control unit must detect and process a miss
  Creates a stall in the pipeline

## Slide 24: Cache Miss (Instruction Memory)
Send the original PC value (current PC – 4) to the memory.
Instruct main memory to perform a read and wait for the memory to complete its access.
Write the cache entry, putting the data from memory in the data portion of the entry, writing the upper bits of the address (from the ALU) into the tag field, and turning the valid bit on.
Restart the instruction execution at the first step, which will refetch the instruction, this time finding it in the cache.

## Slide 25: Cache Miss
Stall until the data is fetched from memory
  Instruction cache miss
    Restart instruction fetch
  Data cache miss
    Complete data access

## Slide 26: Cache Miss
Misses are classified into three different types
Compulsory (cold start)
  First access to a piece of data
  Cannot be avoided
Capacity
  Working set of program is larger than cache size
  Not enough room to cache a locality
Conflict
  collisions, multiple blocks competing for the same space

## Slide 27: Cache Write
If we replace the data memory in our datapath with a cache, what happens on a store word instruction?
If we wrote the data into only the data cache without changing main memory; then main memory would have a different value from that in the cache.
  In such a case, the cache and memory are said to be inconsistent.

## Slide 28: Write-Through
Whenever changes are made to the data in the cache, also change the data in main memory.

## Slide 29: Write-Through
Whenever changes are made to the data in the cache, also change the data in main memory.
Writes take longer
  Suppose 10% of instructions are stores and write to memory takes 100 cycles
  If base CPI = 1, then effective CPI = 1 + 0.1×100 = 11

## Slide 30: Write-Through
Whenever changes are made to the data in the cache, also change the data in main memory.
Writes take longer
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full

## Slide 31: Write-Back
On data-write hit, just update the block in cache
  Keep track of whether each block is “clean” or “dirty”
When a dirty block is replaced
  Write it back to memory
  Can use a write buffer to allow replacing block to be read first

## Slide 32: Write Allocation
What should happen on a write miss?
Alternatives for write-through
  Allocate on miss: fetch the block
  Write around: don’t fetch the block
    Since programs often write a whole block before reading it (e.g., initialization)
For write-back
  Usually fetch the block

## Slide 33: Measuring Cache Performance
Components of CPU time
  Program execution cycles
    Includes cache hit time
  Memory stall cycles
    Mainly from cache misses
CPU time = (CPU cycles + Memory-stall cycles) * Clock cycle time
Memory-stall cycles = Read-stall cycles + Write-stall cycles
Read-stall cycles = Reads/Program * Read miss rate * Read miss penalty
Write-stall cycles = (Writes/Program * write miss rate * write miss penalty) + Write buffer stalls

## Slide 34: Measuring Cache Performance
Components of CPU time
  Program execution cycles
    Includes cache hit time
  Memory stall cycles
    Mainly from cache misses

## Slide 35: Cache Performance Example
Assume an instruction cache miss rate for a program is 2% and a data cache miss rate is 4%. If a processor has a CPI of 2 without any memory stalls and the miss penalty is 100 cycles for all misses, determine how much faster a processor would run with a perfect cache that never missed. Assume the frequency of all loads and stores is 36%.

## Slide 36: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Base CPI (ideal cache) = 2
  Miss penalty = 100 cycles
  Load & stores are 36% of instructions

## Slide 37: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Base CPI (ideal cache) = 2
  Miss penalty = 100 cycles
  Load & stores are 36% of instructions
Determine miss cycles per instruction
  I-cache: 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
  Memory miss cycles = 2 + 1.44 = 3.44

## Slide 38: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Base CPI (ideal cache) = 2
  Miss penalty = 100 cycles
  Load & stores are 36% of instructions
Determine miss cycles per instruction
  I-cache: 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
  Memory miss cycles = 2 + 1.44 = 3.44
Actual CPI = 2 + 3.44 = 5.44

## Slide 39: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Base CPI (ideal cache) = 2
  Miss penalty = 100 cycles
  Load & stores are 36% of instructions
Determine miss cycles per instruction
  I-cache: 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
  Memory miss cycles = 2 + 1.44 = 3.44
Actual CPI = 2 + 3.44 = 5.44
Ideal CPU is 5.44/2 =2.72 times faster

## Slide 40: Performance Considerations
What happens if the processor is made faster, but the memory system is not?
  The amount of time spent on memory stalls will take up an increasing fraction of the execution time
  Amdahl’s law

## Slide 41: Cache Performance Example Revisit
Suppose we speed up the system by reducing its CPI from 2 to 1 without changing the clock rate.
  Actual CPI = 1 + 3.44 = 4.44
  Ideal CPU is 4.44/1 = 4.44 times faster
Amount of time spent on memory stalls increases:
  Before: 3.44/5.44 = 63%
  Now: 4.44/5.44 = 77%

## Slide 42: Performance Considerations
Increasing clock rate without changing the memory system also increases the performance lost due to cache misses.
  Memory stalls account for more CPU cycles

## Slide 43: Performance Considerations
Hit Access Time
  If the hit time increases, the total time to access a word from the memory system will increase.
  Affect by:
    Cache size
    Number of pipeline stages
    Cache organization

## Slide 44: Cache Organizations
Direct mapped
Set associative
Fully associative

## Slide 45: Fully Associative
A block in memory may be associated with any entry in the cache
Requires all entries to be searched at once
Comparator per entry (expensive)

## Slide 46: N-way Set Associative
Each block may go to n locations
Each set contains n entries
Block number determines which set
  (Block number) modulo (#Sets in cache)
Search all entries in a given set at once
n comparators (less expensive)

## Slide 47: Associative Cache Example

## Slide 48: Associativity
All cache organizations are a variation of set associativity.
Direct mapped: 1-way set associative
Fully associative: m-way associative where m is the number of blocks in the cache

## Slide 49: Spectrum of Associativity
For a cache with 8 entries

## Slide 50: Set Associative Cache Organization

## Slide 51: Replacement Policy
Direct mapped: no choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way, manageable for 4-way, too hard beyond that
Random
  Gives approximately the same performance as LRU for high associativity

## Slide 52: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3

## Slide 53: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 

## Slide 54: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 

## Slide 55: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 

## Slide 56: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 

## Slide 57: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 
8 | 0 | miss | Mem[8] |  | Mem[6] | 

## Slide 58: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
5 misses
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 
8 | 0 | miss | Mem[8] |  | Mem[6] | 

## Slide 59: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 

## Slide 60: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 

## Slide 61: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 

## Slide 62: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 

## Slide 63: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 

## Slide 64: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 

## Slide 65: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
2-way set associative
4 misses
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 

## Slide 66: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Fully associative
3 misses
Block address |  | Hit/miss | Cache content after access |  |  | 
0 |  | miss | Mem[0] |  |  | 
8 |  | miss | Mem[0] | Mem[8] |  | 
0 |  | hit | Mem[0] | Mem[8] |  | 
6 |  | miss | Mem[0] | Mem[8] | Mem[6] | 
8 |  | hit | Mem[0] | Mem[8] | Mem[6] | 

## Slide 67: How Much Associativity
Increased associativity decreases miss rate
  But with diminishing returns
Simulation of a system with 64KB cache, 16-word blocks
  1-way: 10.3%
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%

## Slide 68: Multilevel Caches
Primary cache attached to CPU
  Small, but fast
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
Main memory services L-2 cache misses
Some high-end systems include L-3 cache

## Slide 69: Multilevel Cache Example
Suppose we have a processor with a base CPI of 1.0, assuming all references hit in the primary cache, and a clock rate of 5 GHz. Assume a main memory access time of 100 ns, including all the miss handling. Suppose the miss rate per instruction at the primary cache is 2%.
How much faster will the processor be if we add a secondary cache that has a 5 ns access time for either a hit or a miss and is large enough to reduce the miss rate to main memory to 0.5%?

## Slide 70: Multilevel Cache Example
Given
  CPU base CPI = 1
  CPU clock rate = 5 GHz
  Miss rate/instruction = 2%
  Main memory access time = 100ns

## Slide 71: Multilevel Cache Example
Given
  CPU base CPI = 1
  CPU clock rate = 5 GHz
  Miss rate/instruction = 2%
  Main memory access time = 100ns
With just primary cache
  Miss penalty = 100ns/0.2ns = 500 cycles
  Effective CPI = 1 + 0.02 × 500 = 11

## Slide 72: Multilevel Cache Example
Now add L-2 cache
  Access time = 5ns
  Global miss rate to main memory = 0.5%
Primary miss with L-2 hit
  Penalty = 5ns/0.2ns = 25 cycles
Primary miss with L-2 miss
  Extra penalty = 500 cycles
CPI = 1 + 0.02 × 25 + 0.005 × 500 =4
Performance ratio = 11/4 = 2.8

## Slide 73: Multilevel Cache Considerations
Primary cache
  Focus on minimal hit time
L-2 cache
  Focus on low miss rate to avoid main memory access
  Hit time has less overall impact
Results
  L-1 cache usually smaller than a single cache
  L-1 block size smaller than L-2 block size

## Slide 74: Summary
Cost/Performance tradeoff in memory technologies
  Create an illusion of large amounts of fast memory with a hierarchy
  Uses caches close to the processor
Cache Details
  Organization: direct mapped, set associative, fully associative
  Write policy: write-through vs. write-back
  Replacement policy: direct, LRU, random

## Slide 75: Summary
Cache Performance
  Use better technology:
    Use faster RAMs
    Cost and availability are limitations
  Decrease Hit Time
    Make cache smaller, but miss rate increases
    Use direct mapped, but miss rate increases
  Decrease Miss Rate
    Make cache larger, but can increases hit time
    Add associativity, but can increase hit time
    Increase block size, but increases miss penalty
  Decrease Miss Penalty
    Reduce transfer time component of miss penalty
    Add another level of cache

## Slide 76: Virtual Memory
What happens when you want to use more memory than your computer actually has?
  Many programs in memory
  Large programs / Large input files
Use the next level of the memory hierarchy as a cache.

## Slide 77: Virtual Memory
When main memory is set up to act as a cache for the secondary storage it is called virtual memory.
  Allows efficient and safe sharing of memory
  Gives the illusion of a larger main memory
Each program is given a private virtual address space to contain frequently used code and data
  This virtual space is protected from other programs

## Slide 78: Virtual Memory
A virtual memory block is called a page
  Pages can be stored in main memory or on disk
A virtual memory miss is called a page fault
  Occurs when pages are not in main memory
Processors use virtual addresses, which must be translated to physical addresses
  Pages are a fixed size
  A combination of hardware and software is used for translation

## Slide 79: Address Translation
Load/Stores/PC computes a virtual address
Check to see if the page containing the virtual address is in main memory
Compute the physical address
Access memory with the physical address

## Slide 80: Address Translation
A virtual address is made up of the virtual page number and a page offset.

## Slide 81: Page Fault Penalty
On page fault, the page must be fetched from disk
  Takes millions of clock cycles
  Handled by OS code
Design decisions try to minimize page fault rate
  Page size
    Must be large enough to balance high access time
  Memory Organization
    Fully associative placement
  Smart replacement algorithms
    Handled by software because of reduced overhead
  Write policy
    Write-back policy to avoid accessing the disk on every write

## Slide 82: Virtual Memory Writes
Write-back policy, but applied to entire page
  If any word of the page is modified, the whole page is marked dirty
  When the page is replaced, a dirty page must be written to disk
  Copying an entire page is more efficient that copying individual words

## Slide 83: Page Translation
Fully associative organization minimizes page faults but makes it more difficult to locate a page.
Use a data structure to store recent mappings from virtual to physical addresses
  The Page Table

## Slide 84: Page Table
Stores placement information
  Array of page table entries (PTE), indexed by virtual page number
  Page table register in CPU points to page table in physical memory
If page is present in memory
  PTE stores the physical page number
  Plus other status bits (referenced, dirty, …)
If page is not present in memory
  Page fault

## Slide 85: Page Table

## Slide 86: Page Fault
When a page fault occurs, the OS is given control via an exception
The OS must locate the page to be loaded and decide where it should be placed in virtual memory.

## Slide 87: Page Replacement
Most operating systems prefer LRU replacement to reduce page fault rate
  Reference bit (aka use bit) in PTE set to 1 on access to page
  Periodically cleared to 0 by OS
  A page with reference bit = 0 has not been used recently

## Slide 88: Address Translation
Address translation would appear to require extra memory references
  One to access the PTE
  Then the actual memory access
Principle of Locality
  In the page table, when a translation is used it will probably be needed again
  Pages contain a larger section of code and data
    words in a page have both temporal and spatial locality

## Slide 89: Translation Look-aside Buffers
Modern processors include a cache to track recently used translations called the TLB

## Slide 90: TLB Misses
If page is in memory
  Load the PTE from memory and retry
  Can be handled in hardware
If page is not in memory (page fault)
  OS handles fetching the page and updating the page table
  Then restart the faulting instruction
TLB misses more common than page faults
  Retrieve missing translation from page table
  Copy reference and dirty bits of TLB entry back to page table entry

## Slide 91: TLB and Cache Interaction
Virtual memory and cache systems work together as a hierarchy.
  An element cannot be present in a cache unless it is also in main memory.
  When a page is replaced in main memory, it is also flushed from cache.
    All valid bits are set to zero

## Slide 92: TLB and Cache Interaction
Best Case
  Virtual address is translated by TLB
  Physical address leads to cache hit
  Data can be found quickly and sent to the processor
Worst Case
  A reference can miss in all three components
    TLB miss
    Cache miss
    Page table miss

## Slide 93: TLB and Cache Interaction

## Slide 94: TLB and Cache Interaction
Both the cache index and the cache tag are physical
  Hit time now includes TLB access in addition to cache access

## Slide 95: Some more details on TLB Misses
Occurs when no entry of the TLB matches a virtual address
Two possibilities
  The page is in memory, need to create TLB entry
  The page is not in memory, need the OS to load the page

## Slide 96: Some more details on TLB Misses
When a miss occurs
  Check the page table for the desired page table entry
  If the valid bit is zero, there is a page fault
    Remember, the page table has entries for each virtual memory address in the page. Only misses if the page has not been loaded in to main memory.
  If the valid bit is one, update the TLB with the translation

## Slide 97: Some more details on TLB Misses
In MIPS, TLB misses are traditionally handled in software
  Stall the pipeline
  Update the TLB with the correct translation
  Restart the instruction that caused the miss
  Will be a hit this time since we updated the TLB
  Page faults still possible

## Slide 98: Some more details on TLB Misses
Page faults require OS intervention
  Exceptions interrupt the active process and transfer control to the OS
  The exception program counter (EPC) is used to hold the program counter of the instruction to be restarted
  Exceptions must be recognized by the end of the same clock cycle that the memory access occurs
    The next clock cycle must start exception processing

## Slide 99: Some more details on TLB Misses
Page faults require OS intervention
  Look up the page table entry using the virtual address and find the location of the referenced page on disk.
  Choose a physical page to replace; if the chosen page is dirty, it must be written out to disk before we can bring a new virtual page into this physical page.
  Start a read to bring the referenced page from disk into the chosen physical page.

## Slide 100: Some more details on TLB Misses
Misses in the data cache are more difficult
  They occur in the middle of instructions, unlike instruction page faults.
  The instruction cannot be completed before handling the exception.
  After handling the exception, the instruction must be restarted as if nothing had occurred.

## Slide 101: Memory Protection
Different tasks can share parts of their virtual address spaces
  But need to protect against errant access
  Requires OS assistance
Hardware support for OS protection
  Privileged supervisor mode (aka kernel mode)
  Privileged instructions
  Page tables and other state information only accessible in supervisor mode

## Slide 102: Summary
Common principles apply at all levels of the memory hierarchy
  Based on notions of caching
At each level in the hierarchy
  Block placement
  Finding a block
  Replacement on a miss
  Write policy

## Slide 103: Summary
Virtual memory is the name of the level that manages caching between main memory and permanent storage.
  Supports larger programs
  Supports more programs
  Supports sharing between programs
Page faults are very expensive to service
  Pages are large to take advantage of locality
  Pages can be loaded anywhere in memory
  OS can assist with various techniques
  Write-back policy to reduce disk access
Accessing memory takes two accesses now
  Use TLBs to speed the process