## Slide 1: Combinational Logic Design

## Slide 2: Digital Systems
Digital electronics operate with only two voltage levels of interest: a high voltage and a low voltage. All other voltage values are temporary and occur while transitioning between the values.

## Slide 3: Digital Systems
Low voltage is associated with 0s
High voltage is associated with 1s
The actual voltage values may differ from system to system

## Slide 4: Logic Blocks
A simple model of a digital system is a unit with inputs and outputs:
Digital systems consist of an interconnection of electronic switches i.e. a switching network
A switching network performs a set of logical functions in either a combinational or sequential fashion.
inputs
outputs
system

## Slide 5: Combinational vs. Sequential
Combinational:
  No Feedback
  Output defined completely in terms of the Inputs.
Sequential:
  With feedback
  Network goes through different states
  New state depends on Inputs and current state.
T
T

## Slide 6: Combinational vs. Sequential
B
A
C
Clock
Combinational:
  input A, B
  wait for clock edge
  observe C
  wait for another clock edge
  observe C again: will stay the same
Sequential:
  input A, B
  wait for clock edge
  observe C
  wait for another clock edge
  observe C again: may be different

## Slide 7: Combinational logic
Truth Tables, Logic Equations, and Gates
  NOT, AND, OR, NAND, NOR, XOR, . . .
  Minimal set
Axioms and theorems of Boolean algebra
  Proofs by re-writing
  Proofs by perfect induction
Gate logic
  Networks of Boolean functions
  Time behavior
Canonical forms
  Two-level
  Incompletely specified functions
Simplification
  Boolean cubes and Karnaugh maps
  Two-level simplification

## Slide 8: Truth Tables
Combinational logic blocks can be completely specified by defining the output values for each possible set of input values.
This is done using a truth table.
For a logic block with n inputs, there are 2n entries in the truth table. Each entry specifies the value of all the outputs for that particular input combination.

## Slide 9: Truth Tables
Consider a logic function with three inputs, A, B, and C, and three outputs, D, E, and F. The function is defined as follows:
  D is true if at least one input is true
  E is true if exactly two inputs are true
  F is true only if all three inputs are true.

## Slide 10: Truth Tables
Consider a logic function with three inputs, A, B, and C, and three outputs, D, E, and F. The function is defined as follows:
  D is true if at least one input is true
  E is true if exactly two inputs are true
  F is true only if all three inputs are true.
Inputs |  |  | Outputs |  | 
A | B | C | D | E | F
0 | 0 | 0 |  |  | 
0 | 0 | 1 |  |  | 
0 | 1 | 0 |  |  | 
0 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 

## Slide 11: Truth Tables
Consider a logic function with three inputs, A, B, and C, and three outputs, D, E, and F. The function is defined as follows:
  D is true if at least one input is true
  E is true if exactly two inputs are true
  F is true only if all three inputs are true.
Inputs |  |  | Outputs |  | 
A | B | C | D | E | F
0 | 0 | 0 | 0 |  | 
0 | 0 | 1 | 1 |  | 
0 | 1 | 0 | 1 |  | 
0 | 1 | 1 | 1 |  | 
1 | 0 | 0 | 1 |  | 
1 | 0 | 1 | 1 |  | 
1 | 1 | 0 | 1 |  | 
1 | 1 | 1 | 1 |  | 

## Slide 12: Truth Tables
Consider a logic function with three inputs, A, B, and C, and three outputs, D, E, and F. The function is defined as follows:
  D is true if at least one input is true
  E is true if exactly two inputs are true
  F is true only if all three inputs are true.
Inputs |  |  | Outputs |  | 
A | B | C | D | E | F
0 | 0 | 0 | 0 | 0 | 
0 | 0 | 1 | 1 | 0 | 
0 | 1 | 0 | 1 | 0 | 
0 | 1 | 1 | 1 | 1 | 
1 | 0 | 0 | 1 | 0 | 
1 | 0 | 1 | 1 | 1 | 
1 | 1 | 0 | 1 | 1 | 
1 | 1 | 1 | 1 | 0 | 

## Slide 13: Truth Tables
Consider a logic function with three inputs, A, B, and C, and three outputs, D, E, and F. The function is defined as follows:
  D is true if at least one input is true
  E is true if exactly two inputs are true
  F is true only if all three inputs are true.
Inputs |  |  | Outputs |  | 
A | B | C | D | E | F
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 1 | 0 | 1

## Slide 14: Possible Logic Functions
There are 16 possible functions of 2 input variables:
  in general, there are functions of n inputs
X
Y
F
X nand Y not (X and Y)
        X Y 16 possible functions (F0–F15) 0 0 0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1 0 1 0 0 0 0 1 1 1 1 0 0 0 0 1 1 1 1
        1 0 0 0 1 1 0 0 1 1 0 0 1 1 0 0 1 1
        1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
0
X and Y
X
Y
X or Y
not Y
not X
1
X xor Y
X nor Y not (X or Y)
X xnor Y

## Slide 15: Boolean Algebra
Deals with a set of variables (operands) combined with a set of operators.
  Variables denoted by X,Y,Z, etc.
  Variables take binary values:
    Either “0” or “1” (“false” or “true”)
Operators: NOT, AND, OR
All logical operations can be described using these three operators.

## Slide 16: OR
The OR operator is written as +, as in A + B.
The OR operation is also called a logical sum.
A | B | A + B (OR)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 17: AND
The AND operator is written as *, as in A * B.
The AND operation is also called a logical product.
A | B | A * B (AND)
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 18: NOT
The unary operator NOT is written as A’.
A | A’
0 | 1
1 | 0

## Slide 19: Axioms and theorems of Boolean algebra
Identity
  X + 0 = X
  X • 1 = X
Null
  X + 1 = 1
  X • 0 = 0
Idempotency:
  X + X = X
  X • X = X
Involution:
  (X')' = X
Inverse:
  X + X' = 1
  X • X' = 0
Commutative:
  X + Y = Y + X
  X • Y = Y • X
Associativity:
  (X + Y) + Z = X + (Y + Z)
  (X • Y) • Z = X • (Y • Z)

## Slide 20: Axioms and theorems of Boolean algebra
Distributivite:
  X • (Y + Z) = (X • Y) + (X • Z)
  X + (Y • Z) = (X + Y) • (X + Z)
Uniting:
  X • Y + X • Y' = X
  (X + Y) • (X + Y') = X
Absorption:
  X + X • Y = X
  X • (X + Y) = X
  (X + Y') • Y = X • Y
  (X • Y') + Y = X + Y

## Slide 21: Axioms and theorems of Boolean algebra
Factoring:
  (X + Y) • (X' + Z) =X • Z + X' • Y
  X • Y + X' • Z = (X + Z) • (X' + Y)
Consensus:
(X • Y) + (Y • Z) + (X' • Z) = X • Y + X' • Z
(X + Y) • (Y + Z) • (X' + Z) = (X + Y) • (X' + Z)
de Morgan's:
  (X + Y + ...)' = X' • Y' • ...
  (X • Y • ...)' = X' + Y' + ...

## Slide 22: Duality
The Dual of a Boolean expression is derived by replacing • by +, + by •, 0 by 1, and 1 by 0, and leaving variables unchanged.
Any theorem that can be proven is thus also proven for its dual!
duality:
  X + Y + ...  X • Y • ...
Different than deMorgan’s Law
  this is a statement about theorems (metatheorem)
  this is not a way to manipulate (re-write) expressions

## Slide 23: Logic functions and Boolean algebra
X, Y are Boolean algebra variables
X Y X' Y' X • Y X' • Y' ( X • Y ) + ( X' • Y' ) 0 0 1 1 0 1 1 0 1 1 0 0 0 0 1 0 0 1 0 0 0
1 1 0 0 1 0 1
( X • Y ) + ( X' • Y' ) = X  Y
X Y X • Y 0 0 0 0 1 0 1 0 0
1 1 1
X Y X' X' • Y 0 0 1 0 0 1 1 1 1 0 0 0
1 1 0 0
Boolean expression that is true when the variables X and Y have the same value
and false, otherwise
Any logic function that can be expressed as a truth table can be written as an expression in Boolean algebra using the operators: ', +, and •

## Slide 24: Logic functions and Boolean algebra
D is true if at least one input is true
E is true if exactly two inputs are true
F is true only if all three inputs are true.
D = A+B+C
F = A*B*C
E = ((A * B) + (A * C) + (B * C)) * (A * B * C )’
E = (A * B * C’ ) + (A * C * B’ ) + (B * C * A’ )
Inputs |  |  | Outputs |  | 
A | B | C | D | E | F
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 1 | 0 | 1

## Slide 25: Proving theorems with Perfect Induction
(X + Y)' = X' • Y' NOR is equivalent to AND with inputs complemented
(X • Y)' = X' + Y' NAND is equivalent to OR with inputs complemented
X Y X' Y' (X + Y)' X' • Y' 0 0 1 1 0 1 1 0
1 0 0 1
1 1 0 0
X Y X' Y' (X • Y)' X' + Y' 0 0 1 1
0 1 1 0 1 0 0 1
1 1 0 0
Using perfect induction (complete truth table):
  e.g., de Morgan's:
1
0
0
0
1
1
1
0
1
0
0
0
1
1
1
0

## Slide 26: Proving theorems with Perfect Induction
E = ((A * B) + (A * C) + (B * C)) * (A * B * C )’
E = (A * B * C’ ) + (A * C * B’ ) + (B * C * A’ )
Inputs |  |  | E |  | 
A | B | C | E | ((A * B) + (A * C) + (B * C)) * (A * B * C )’ | (A * B * C’ ) + (A * C * B’ ) + (B * C * A’ )
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0

## Slide 27: Proving theorems with Rewriting
Using the axioms of Boolean algebra:
  e.g., prove the theorem: X • Y + X • Y' = X
  e.g., prove the theorem: X + X • Y = X
Distributive law X • Y + X • Y' = X • (Y + Y')
Inverse law X • (Y + Y') = X • (1)
Identity law X • (1) = X ü
Identity law X + X • Y = X • 1 + X • Y
Distributive law X • 1 + X • Y = X • (1 + Y)
Null law X • (1 + Y) = X • (1)
Identity law X • (1) = X ü

## Slide 28: Proving theorems with Rewriting
E = ((A * B) + (A * C) + (B * C)) * (A * B * C )’
E = (A * B * C’ ) + (A * C * B’ ) + (B * C * A’ )
((A * B) + (A * C) + (B * C)) * (A * B * C )’
= ((A · B) + (A · C) + (B · C)) * (A’ + B’ + C’)
DeMorgan’s law
= (A’ + B’ + C’)(A*B) + (A’ + B’ + C’)(A*C) + (A’ + B’ + C’)(B*C)
Distributive law
= (A*B*A’) + (A*B*B’) + (A*B*C’) + (A*C*A’) + (A*C*B’) + (A*C*C’) + (B*C*A’)+(B*C*B’)+(B*C*C’)
Distributive law
= (0*B)+(0*A)+(A*B*C’) + (0*C)+(A*C*B’)+(A*0) + (B*C*A’)+(C*0)+(B*0) Inverse law
= 0 + 0 + (A*B*C’) + 0 +(A*C*B’) + 0 + (B*C*A’) + 0 +0
Null law
= (A · B ·C’ ) + (A · C ·B’ ) + (B · C ·A’ )
Identity law

## Slide 29: Adder, Part 1
1-bit binary adder
  inputs: A, B, Carry-in
  outputs: Sum, Carry-out
A
B
Cin
Cout
A B Cin Cout
0 0 0 0 0 1
0 1 0
0 1 1
1 0 0 1 0 1
1 1 0
1 1 1
0
1
1
0
1
0
0
1
0
0
0
1
0
1
1
1
Cout = A' B Cin + A B' Cin + A B Cin' + A B Cin
= A' B' Cin + A' B Cin' + A B' Cin' + A B Cin

## Slide 30: Apply the theorems to simplify expressions
The theorems of Boolean algebra can simplify Boolean expressions
  The Cout function is used as an example here, but the same rules apply to any function.
Cout = A' B Cin + A B' Cin + A B Cin' + A B Cin
= A' B Cin + A B' Cin + A B Cin' + A B Cin + A B Cin
= A' B Cin + A B Cin + A B' Cin + A B Cin' + A B Cin
= (A' + A) B Cin + A B' Cin + A B Cin' + A B Cin
= (1) B Cin + A B' Cin + A B Cin' + A B Cin
= B Cin + A B' Cin + A B Cin' + A B Cin + A B Cin
= B Cin + A B' Cin + A B Cin + A B Cin' + A B Cin
= B Cin + A (B' + B) Cin + A B Cin' + A B Cin
= B Cin + A (1) Cin + A B Cin' + A B Cin
= B Cin + A Cin + A B (Cin' + Cin)
= B Cin + A Cin + A B (1)
= B Cin + A Cin + A B

## Slide 31: Logic Gates
NOT X' X ~X
AND X • Y X  Y
OR X + Y X  Y
X Y Z 0 0 0 0 1 0 1 0 0
1 1 1
X Y 0 1 1 0
X Y Z 0 0 0 0 1 1 1 0 1
1 1 1
X
Y
X
X
Y
Y
Z
Z

## Slide 32: Logic Gates and Inverters
Rather than draw inverters explicitly, a common practice is to add “bubbles” to the inputs or outputs of a gate to cause the logic value on that input line or output line to be inverted.

## Slide 33: Logic Gates
X
Y
Z
X Y Z 0 0 1 0 1 1 1 0 1
1 1 0
X Y Z 0 0 1 0 1 0 1 0 0
1 1 0
Z
X
Y
X
Y
Z
X Y Z 0 0 1 0 1 0 1 0 0
1 1 1
X Y Z 0 0 0 0 1 1 1 0 1
1 1 0
Z
X
Y
X xor Y = X Y' + X' Y X or Y but not both ("inequality", "difference")
X xnor Y = X Y + X' Y' X and Y are the same ("equality", "coincidence")
NAND
NOR
XOR X Y
XNOR X  Y

## Slide 34: Logic Gates
More than one way to map expressions to gates
  e.g., Z = A' • B' • (C + D) = (A' • (B' • (C + D)))
T1
T2
use of 3-input gate
A
B
C
D
T2
T1
Z
A
B
C
D
Z

## Slide 35: Different realizations of a function
A B C Z 0 0 0 0
0 0 1 1
0 1 0 0
0 1 1 1
1 0 0 0
1 0 1 1
1 1 0 1
1 1 1 0
two-level realization (we don't count NOT gates)
XOR gate (easier to draw but costlier to build)
multi-level realization (gates with fewer inputs)

## Slide 36: Which realization is best?
Reduce number of inputs
  literal: input variable (complemented or not)
    can approximate cost of logic gate as 2 transistors per literal
    why not count inverters?
  Fewer literals means less transistors
    smaller circuits and reduced electric connections
  Fewer inputs implies faster gates
    gates are smaller and thus also faster
  Fan-ins (# of gate inputs) are limited in some technologies
Reduce number of gates
  Fewer gates (and the packages they come in) means smaller circuits

## Slide 37: Which realization is best?
Reduce number of levels of gates
  Fewer level of gates implies reduced signal propagation delays
  Minimum delay configuration typically requires more gates
    wider, less deep circuits
How do we explore tradeoffs between increased circuit delay and size?
  Automated tools to generate different solutions
  Logic minimization: reduce number of gates and complexity
  Logic optimization: reduction while trading off against delay

## Slide 38: Universal Gates
We can implement all logic functions from NOT, NOR, and NAND gates.
  For example, implementing X and Y is the same as implementing not (X nand Y)
In fact, we can do it with only NOR or only NAND
  NOT is just a NAND or a NOR with both inputs tied together
  and NAND and NOR are "duals", i.e., easy to implement one using the other
X Y X nand Y 0 0 1 1 1 0
X Y X nor Y 0 0 1 1 1 0
X nand Y  not ( (not X) nor (not Y) ) X nor Y  not ( (not X) nand (not Y) )

## Slide 39: Universal Gates
Because NOT, NOR, and NAND are the cheapest they are the functions we implement the most in practice

## Slide 40: Adder, Part 2
Logic gates for Sum (shown without Cin)
Sum = A' B + A B’
A B Sum
0 0 0 1
1 0
1 1
0
1
1
0

## Slide 41: Adder, Part 2
Logic gates for Cout (shown without Cin)
A B Cout
0 0 1 0 0 1
1 1
0
0
0
1
Cout = A B

## Slide 42: Adder, Part 2
Logic gates for Sum and Cout (shown without Cin)

## Slide 43: Decoders
A decoder is a logic block that takes in an n-bit input and selects from 2n outputs.
  One output is asserted for each possible input combination.
  Outputs are labeled Out0, Out1, …, Out2n – 1
  If the input is k, then Outk will be true

## Slide 44: Decoders

## Slide 45: Multiplexors
A multiplexor is a logic block that takes in n inputs and selects one to be the output.
  Could also be called a selector
  The output is one of the inputs, selected by a control value.

## Slide 46: Multiplexors
A multiplexor is a logic block that takes in n inputs and selects one to be the output.
  Could also be called a selector
  The output is one of the inputs, selected by a control value.

## Slide 47: Multiplexors
Multiplexors can be created with an arbitrary number of data inputs.
MULTIPLEXOR
1 output
2n inputs
n selection lines

## Slide 48: 4-to-1 Multiplexor
MULTIPLEXOR
Output
4 Inputs
S0
S1
I0
I1
I2
I3
S1 S0
Output
0 0
0 1
1 0
1 1
I0
I1
I2
I3

## Slide 49: 4-to-1 Multiplexor
Logic Gates

## Slide 50: Canonical forms
Any logic function can be implemented with only AND, OR, and NOT functions.
Any logic function can be written in canonical form, where every input is either a true or complemented variable and there are only two levels of gates
  AND and OR

## Slide 51: Canonical forms
Truth table is the unique signature of a Boolean function
Many alternative gate realizations may have the same truth table
Canonical forms
  Standard forms for a Boolean expression
  Provides a unique algebraic signature

## Slide 52: Canonical forms
These are called two-level representations
  sum of products
    A logical sum (OR) of products (terms using the AND operator)
  product of sums
    A logical product (AND) of sums (terms using the OR operator)

## Slide 53: Canonical forms
From a previous example:
  E = ((A · B) + (A · C) + (B · C)) · (A · B · C )’
    Requires three levels of logic (not a canonical form)
  E = (A · B ·C’ ) + (A · C ·B’ ) + (B · C ·A’ )
    Sum of product form

## Slide 54: Sum-of-products canonical form
Also known as disjunctive normal form
Also known as minterm expansion
F =
A B C F F' 0 0 0 0 1
0 0 1 1 0
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 0
F' = A'B'C' + A'BC' + AB'C'
F = 001 011 101 110 111
+ A'BC
+ AB'C
+ ABC'
+ ABC
A'B'C

## Slide 55: Sum-of-products canonical form
short-hand notation for minterms of 3 variables
A B C minterms 0 0 0 A'B'C' m0
0 0 1 A'B'C m1
0 1 0 A'BC' m2
0 1 1 A'BC m3
1 0 0 AB'C' m4
1 0 1 AB'C m5
1 1 0 ABC' m6
1 1 1 ABC m7
F in canonical form: F(A, B, C) = m(1,3,5,6,7) = m1 + m3 + m5 + m6 + m7
= A'B'C + A'BC + AB'C + ABC' + ABC
canonical form  minimal form F(A, B, C) = A'B'C + A'BC + AB'C + ABC + ABC'
      = (A'B' + A'B + AB' + AB)C + ABC'
      = ((A' + A)(B' + B))C + ABC' = C + ABC' = ABC' + C
= AB + C
Product term (or minterm)
  ANDed product of literals – input combination for which output is true
  Each variable appears exactly once, in true or inverted form (but not both)

## Slide 56: Sum-of-products canonical form
Inputs |  |  | Output
A | B | C | D
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 57: Sum-of-products canonical form
A’ * B’ * C
Inputs |  |  | Output
A | B | C | D
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 58: Sum-of-products canonical form
A’ * B’ * C
A’ * B * C’
Inputs |  |  | Output
A | B | C | D
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 59: Sum-of-products canonical form
A’ * B’ * C
A’ * B * C’
A * B’ * C’
Inputs |  |  | Output
A | B | C | D
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 60: Sum-of-products canonical form
A’ * B’ * C
A’ * B * C’
A * B’ * C’
A * B * C
Inputs |  |  | Output
A | B | C | D
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 61: Sum-of-products canonical form
D = (A’ * B’ * C) + (A’ * B * C’) + (A * B’ * C’) + (A * B * C)
Inputs |  |  | Output
A | B | C | D
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 62: Product-of-sums canonical form
F = 000 010 100 F =
F' = (A + B + C') (A + B' + C') (A' + B + C') (A' + B' + C) (A' + B' + C')
Also known as conjunctive normal form
Also known as maxterm expansion
A B C F F' 0 0 0 0 1
0 0 1 1 0
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 0
(A + B + C)
(A + B' + C)
(A' + B + C)

## Slide 63: Product-of-sums canonical form
A B C maxterms 0 0 0 A+B+C M0
0 0 1 A+B+C' M1
0 1 0 A+B'+C M2
0 1 1 A+B'+C' M3
1 0 0 A'+B+C M4
1 0 1 A'+B+C' M5
1 1 0 A'+B'+C M6
1 1 1 A'+B'+C' M7
short-hand notation for maxterms of 3 variables
F in canonical form: F(A, B, C) = M(0,2,4) = M0 • M2 • M4
= (A + B + C) (A + B' + C) (A' + B + C)
canonical form  minimal form F(A, B, C) = (A + B + C) (A + B' + C) (A' + B + C)
      = (A + B + C) (A + B' + C)
      (A + B + C) (A' + B + C)
      = (A + C) (B + C)
Sum term (or maxterm)
  ORed sum of literals – input combination for which output is false
  each variable appears exactly once, in true or inverted form (but not both)

## Slide 64: Product-of-sums canonical form
Inputs |  |  | Output
A | B | C | D
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 65: Product-of-sums canonical form
A + B + C
Inputs |  |  | Output
A | B | C | D
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 66: Product-of-sums canonical form
A + B + C
A + B’ + C’
Inputs |  |  | Output
A | B | C | D
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 67: Product-of-sums canonical form
A + B + C
A + B’ + C’
A’ + B + C’
Inputs |  |  | Output
A | B | C | D
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 68: Product-of-sums canonical form
A + B + C
A + B’ + C’
A’ + B + C’
A’ + B’ + C
Inputs |  |  | Output
A | B | C | D
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 69: Product-of-sums canonical form
D= (A + B + C)(A + B’ + C’)(A’ + B + C’)(A’ + B’ + C)
Inputs |  |  | Output
A | B | C | D
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 70: Four alternative two-level implementations of F = AB + C
canonical sum-of-products minimized sum-of-products canonical product-of-sums minimized product-of-sums
F1
F2
F3
B
A
C
F4

## Slide 71: Mapping between canonical forms
Minterm to maxterm conversion
  Use maxterms whose indices do not appear in minterm expansion
  e.g., F(A,B,C) = m(1,3,5,6,7) = M(0,2,4)
Maxterm to minterm conversion
  Use minterms whose indices do not appear in maxterm expansion
  e.g., F(A,B,C) = M(0,2,4) = m(1,3,5,6,7)
Minterm expansion of F to minterm expansion of F'
  Use minterms whose indices do not appear
  e.g., F(A,B,C) = m(1,3,5,6,7) F'(A,B,C) = m(0,2,4)
Maxterm expansion of F to maxterm expansion of F'
  Use maxterms whose indices do not appear
  e.g., F(A,B,C) = M(0,2,4) F'(A,B,C) = M(1,3,5,6,7)

## Slide 72: S-o-P, P-o-S, and de Morgan’s theorem
Sum-of-products
  F' = A'B'C' + A'BC' + AB'C‘
Apply de Morgan's
  (F')' = (A'B'C' + A'BC' + AB'C')'
  F = (A + B + C) (A + B' + C) (A' + B + C)
Product-of-sums
  F' = (A + B + C') (A + B' + C') (A' + B + C') (A' + B' + C) (A' + B' + C')
Apply de Morgan's
  (F')' = ( (A + B + C')(A + B' + C')(A' + B + C')(A' + B' + C)(A' + B' + C') )'
  F = A'B'C + A'BC + AB'C + ABC' + ABC

## Slide 73: Programmable Logic Array
The relationship between a truth table and a two-level representation allows us to generate a gate-level implementation of any set of logic functions.
The sum-of-products corresponds to a programmable logic array.

## Slide 74: Programmable Logic Array

## Slide 75: Programmable Logic Array
Efficient Characteristics
  only the truth table entries that produce a true value for at least one output have any logic gates associated with them.
  each different product term will have only one entry in the PLA, even if the product term is used in multiple outputs.

## Slide 76: Programmable Logic Array
Inputs |  |  | Outputs |  | 
A | B | C | D | E | F
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 1 | 0 | 1

## Slide 77: Programmable Logic Array

## Slide 78: Incompleteley specified functions
Example: binary coded decimal increment by 1
  BCD digits encode decimal digits 0 – 9 in bit patterns 0000 – 1001
A B C D W X Y Z 0 0 0 0 0 0 0 1
0 0 0 1 0 0 1 0
0 0 1 0 0 0 1 1
0 0 1 1 0 1 0 0
0 1 0 0 0 1 0 1
0 1 0 1 0 1 1 0
0 1 1 0 0 1 1 1
0 1 1 1 1 0 0 0
1 0 0 0 1 0 0 1
1 0 0 1 0 0 0 0
1 0 1 0 X X X X
1 0 1 1 X X X X
1 1 0 0 X X X X
1 1 0 1 X X X X
1 1 1 0 X X X X
1 1 1 1 X X X X
off-set of W
these input patterns should never be encountered in practice – "don't care" about associated output values, can be exploited in minimization
don't care (DC) set of W
on-set of W

## Slide 79: Notation for incompletely specified functions
Don't cares and canonical forms
  So far, only represented on-set
  Also represent don't-care-set
  Need two of the three sets (on-set, off-set, dc-set)
Canonical representations of the BCD increment by 1 function:
  Z = m0 + m2 + m4 + m6 + m8 + d10 + d11 + d12 + d13 + d14 + d15
  Z =  [ m(0,2,4,6,8) + d(10,11,12,13,14,15) ]
  Z = M1 • M3 • M5 • M7 • M9 • D10 • D11 • D12 • D13 • D14 • D15
  Z =  [ M(1,3,5,7,9) • D(10,11,12,13,14,15) ]

## Slide 80: Simplification of two-level combinational logic
Finding a minimal sum of products or product of sums realization
  Exploit don't care information in the process
Algebraic simplification
  Not an algorithmic/systematic procedure
  How do you know when the minimum realization has been found?
Computer-aided design tools
  Precise solutions require very long computation times, especially for functions with many inputs (> 10)
  Heuristic methods employ "educated guesses" to reduce amount of computation and yield good if not best solutions
Hand methods still relevant
  To understand automatic tools and their strengths and weaknesses
  Ability to check results (on small examples)

## Slide 81: The uniting theorem
A B F
0 0 1
0 1 0
1 0 1
1 1 0
B has the same value in both on-set rows – B remains
A has a different value in the two rows – A is eliminated
F = A'B'+AB' = (A'+A)B' = B'
Key tool to simplification: A (B' + B) = A
Essence of simplification of two-level logic
  Find two element subsets of the ON-set where only one variable changes its value – this single varying variable can be eliminated and a single product term used to represent both elements

## Slide 82: Boolean cubes
1-cube
X
0
1
Visual technique for identifying when the uniting theorem can be applied
n input variables = n-dimensional "cube"
2-cube
X
Y
11
00
01
10
3-cube
X
Y
Z
000
111
101
4-cube
W
X
Y
Z
0000
1111
1000
0111

## Slide 83: Mapping truth tables onto Boolean cubes
A B F
0 0 1
0 1 0
1 0 1
1 1 0
ON-set = solid nodes OFF-set = empty nodes DC-set = 'd nodes
two faces of size 0 (nodes) combine into a face of size 1(line)
A varies within face, B does not this face represents the literal B'
Uniting theorem combines two "faces" of a cube into a larger "face"
Example:
A
B
11
00
01
10
F

## Slide 84: Three variable example
A B Cin Cout
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 1
1 0 0 0
1 0 1 1
1 1 0 1
1 1 1 1
(A'+A)BCin
AB(Cin'+Cin)
A(B+B')Cin
Cout = BCin+AB+ACin
the on-set is completely covered by the combination (OR) of the subcubes of lower dimensionality - note that “111” is covered three times
Binary full-adder carry-out logic
A
B
C
000
111
101

## Slide 85: Higher dimensional cubes
F(A,B,C) = m(4,5,6,7)
on-set forms a square i.e., a cube of dimension 2
represents an expression in one variable i.e., 3 dimensions – 2 dimensions
A is asserted (true) and unchanged
B and C vary
This subcube represents the
literal A
Sub-cubes of higher dimension than 2
A
B
C
000
111
101
100
001
010
011
110

## Slide 86: m-dimensional cubes in a n-dimensional Boolean space
In a 3-cube (three variables):
  0-cube, i.e., a single node, yields a term in 3 literals
  1-cube, i.e., a line of two nodes, yields a term in 2 literals
  2-cube, i.e., a plane of four nodes, yields a term in 1 literal
  3-cube, i.e., a cube of eight nodes, yields a constant term "1"
In general,
  m-subcube within an n-cube (m < n) yields a term with n – m literals

## Slide 87: Karnaugh maps
A B F
0 0 1
0 1 0
1 0 1
1 1 0
Flat map of Boolean cube
  Wrap–around at edges
  Hard to draw and visualize for more than 4 dimensions
  Virtually impossible for more than 6 dimensions
Alternative to truth-tables to help visualize adjacencies
  Guide to applying the uniting theorem
  On-set elements with only one variable changing value are adjacent unlike the situation in a linear truth-table
0 2
1 3
0
1
A
B
0
1
1
0
0
1

## Slide 88: Karnaugh maps (cont’d)
Numbering scheme based on Gray–code
  e.g., 00, 01, 11, 10
  Only a single bit changes in code for adjacent map cells
0 2
1 3
00
01
AB
C
0
1
6 4
7 5
11
10
C
B
A
0 2
1 3
6 4
7 5
C
B
A
0 4
1 5
12 8
13 9
D
A
3 7
2 6
15 11
14 10
C
B
13 = 1101= ABC’D

## Slide 89: Adjacencies in Karnaugh maps
Wrap from first to last column
Wrap top row to bottom row
000 010
001 011
110 100
111 101
C
B
A
A
B
C
000
111
101
100
001
010
011
110

## Slide 90: Karnaugh map examples
We can obtain the complement of the function by covering 0s with subcubes
F =
Cout =
f(A,B,C) = m(0,4,5,7)
0 0
0 1
1 0
1 1
Cin
B
A
1 1
0 0
B
A
1 0
0 0
0 1
1 1
C
B
A
B’
AB
AC
+ ACin
+ BCin
+ B’C’
+ AB’

## Slide 91: More Karnaugh map examples
F(A,B,C) = m(0,4,5,7)
F'(A,B,C) =  m(1,2,3,6)
F' simply replace 1's with 0's and vice versa
G(A,B,C) =
0 0
0 0
1 1
1 1
C
B
A
1 0
0 0
0 1
1 1
C
B
A
0 1
1 1
1 0
0 0
C
B
A
A
= AC + B’C’
= BC’ + A’C

## Slide 92: Karnaugh map: 4-variable example
C
+ B’D’
find the smallest number of the largest possible subcubes to cover the ON-set
(fewer terms with fewer inputs per term)
F(A,B,C,D) = m(0,2,3,5,6,7,8,10,11,14,15) F =
D
A
B
D
A
B
C
0000
1111
1000
0111
1 0
0 1
0 1
0 0
1 1
1 1
1 1
1 1
C
+ A’BD

## Slide 93: Karnaugh maps: don’t cares
f(A,B,C,D) = m(1,3,5,7,9) + d(6,12,13)
  without don't cares
    f =
+ B’C’D
0 0
1 1
X 0
X 1
D
A
1 1
0 X
0 0
0 0
B
C
A’D

## Slide 94: Karnaugh maps: don’t cares
f(A,B,C,D) = m(1,3,5,7,9) + d(6,12,13)
  f = A'D + B'C'D without don't cares
  f = with don't cares
don't cares can be treated as 1s or 0s depending on which is more advantageous
0 0
1 1
X 0
X 1
D
A
1 1
0 X
0 0
0 0
B
C
A'D
by using don't care as a "1" a 2-cube can be formed rather than a 1-cube to cover this node
+ C'D

## Slide 95: Design example: two-bit comparator
we'll need a 4-variable Karnaugh map for each of the 3 output functions
block diagram
LT EQ GT
A B < C D A B = C D A B > C D
A
B
C
D
N1
N2
A B C D LT EQ GT
0 0 0 0 0 1 0
0 1 1 0 0
1 0 1 0 0
1 1 1 0 0
0 1 0 0 0 0 1
0 1 0 1 0
1 0 1 0 0
1 1 1 0 0
1 0 0 0 0 0 1
0 1 0 0 1
1 0 0 1 0
1 1 1 0 0
1 1 0 0 0 0 1
0 1 0 0 1
1 0 0 0 1
1 1 0 1 0
and
truth table

## Slide 96: Design example: two-bit comparator
A' B' D + A' C + B' C D
B C' D' + A C' + A B D'
LT =
EQ =
GT =
K-map for EQ
K-map for LT
K-map for GT
0 0
1 0
0 0
0 0
D
A
1 1
1 1
0 1
0 0
B
C
1 0
0 1
0 0
0 0
D
A
0 0
0 0
1 0
0 1
B
C
0 1
0 0
1 1
1 1
D
A
0 0
0 0
0 0
1 0
B
C
= (A xnor C) • (B xnor D)
LT and GT are similar (flip A/C and B/D)
A' B' C' D' + A' B C' D + A B C D + A B' C D’

## Slide 97: Design example: two-bit comparator
two alternative
implementations of EQ
with and without XOR
XNOR is implemented with at least 3 simple gates
A B C D
EQ
EQ

## Slide 98: Design example: 2x2-bit multiplier
block diagram
and
truth table
4-variable K-map
for each of the 4
output functions
A2 A1 B2 B1 P8 P4 P2 P1
0 0 0 0 0 0 0 0
0 1 0 0 0 0
1 0 0 0 0 0
1 1 0 0 0 0
0 1 0 0 0 0 0 0
0 1 0 0 0 1
1 0 0 0 1 0
1 1 0 0 1 1
1 0 0 0 0 0 0 0
0 1 0 0 1 0
1 0 0 1 0 0
1 1 0 1 1 0
1 1 0 0 0 0 0 0
0 1 0 0 1 1 1 0 0 1 1 0
1 1 1 0 0 1
P1
P2 P4
P8
A1
A2 B1
B2

## Slide 99: Design example: 2x2-bit multiplier (cont’d)
K-map for P8
K-map for P4
K-map for P2
K-map for P1
0 0
0 0
0 0
0 0
B1
A2
0 0
0 0
0 1
1 1
A1
B2
0 0
0 1
0 0
1 0
B1
A2
0 1
0 0
1 0
0 0
A1
B2
0 0
0 0
0 0
1 1
B1
A2
0 1
0 1
0 1
1 0
A1
B2
0 0
0 0
0 0
0 0
B1
A2
0 0
0 0
1 0
0 0
A1
B2
P8 = A2A1B2B1
P4 = A2B2B1' + A2A1'B2
P2 = A2'A1B2 + A1B2B1' + A2B2'B1 + A2A1'B1
P1 = A1B1

## Slide 100: Design example: BCD increment by 1
I8 I4 I2 I1 O8 O4 O2 O1 0 0 0 0 0 0 0 1
0 0 0 1 0 0 1 0
0 0 1 0 0 0 1 1
0 0 1 1 0 1 0 0
0 1 0 0 0 1 0 1
0 1 0 1 0 1 1 0
0 1 1 0 0 1 1 1
0 1 1 1 1 0 0 0
1 0 0 0 1 0 0 1
1 0 0 1 0 0 0 0
1 0 1 0 X X X X
1 0 1 1 X X X X
1 1 0 0 X X X X
1 1 0 1 X X X X
1 1 1 0 X X X X
1 1 1 1 X X X X
block diagram
and
truth table
4-variable K-map for each of the 4 output functions
O1
O2 O4
O8
I1
I2 I4
I8

## Slide 101: Design example: BCD increment by 1 (cont’d)
O8 = I4 I2 I1 + I8 I1'
O4 = I4 I2' + I4 I1' + I4’ I2 I1 O2 = I8’ I2’ I1 + I2 I1'
O1 = I1'
O8
O4
O2
O1
0 0
0 0
X 1
X 0
I1
I8
0 1
0 0
X X
X X
I4
I2
0 0
1 1
X 0
X 0
I1
I8
0 0
1 1
X X
X X
I4
I2
0 1
0 1
X 0
X 0
I1
I8
1 0
0 1
X X
X X
I4
I2
1 1
0 0
X 1
X 0
I1
I8
0 0
1 1
X X
X X
I4
I2

## Slide 102: Definition of terms for two-level simplification
Implicant
  Single element of ON-set or DC-set or any group of these elements that can be combined to form a subcube
Prime implicant
  Implicant that can't be combined with another to form a larger subcube
Essential prime implicant
  Prime implicant is essential if it alone covers an element of ON-set
  Will participate in ALL possible covers of the ON-set
  DC-set used to form prime implicants but not to make implicant essential
Objective:
  Grow implicant into prime implicants (minimize literals per term)
  Cover the ON-set with as few prime implicants as possible (minimize number of product terms)

## Slide 103: Examples to illustrate terms
0 X
1 1
1 0
1 0
D
A
1 0
0 0
1 1
1 1
B
C
5 prime implicants: BD, ABC', ACD, A'BC, A'C'D
0 0
1 1
1 0
1 0
D
A
0 1
0 1
1 1
0 0
B
C
6 prime implicants: A'B'D, BC', AC, A'C'D, AB, B'CD
minimum cover: AC + BC' + A'B'D
essential
minimum cover: 4 essential implicants
essential

## Slide 104: Algorithm for two-level simplification
To get the minimum sum-of-products expression from a Karnaugh map:
  Step 1: choose an element of the ON-set
  Step 2: find "maximal" groupings of 1s and Xs adjacent to that element
    consider top/bottom row, left/right column, and corner adjacencies
    this forms prime implicants (number of elements always a power of 2)
  Repeat Steps 1 and 2 to find all prime implicants
  Step 3: revisit the 1s in the K-map
    if covered by single prime implicant, it is essential, and participates in final cover
    1s covered by essential prime implicant do not need to be revisited
  Step 4: if there remain 1s not covered by essential prime implicants
    select the smallest number of prime implicants that cover the remaining 1s

## Slide 105: Algorithm for two-level simplification (example)
X 1
0 1
0 1
1 1
D
A
0 X
0 1
X 0
0 1
B
C
3 primes around AB'C'D'
X 1
0 1
0 1
1 1
D
A
0 X
0 1
X 0
0 1
B
C
2 primes around A'BC'D'
X 1
0 1
0 1
1 1
D
A
0 X
0 1
X 0
0 1
B
C
2 primes around ABC'D
X 1
0 1
0 1
1 1
D
A
0 X
0 1
X 0
0 1
B
C
minimum cover (3 primes)
X 1
0 1
0 1
1 1
D
A
0 X
0 1
X 0
0 1
B
C
X 1
0 1
0 1
1 1
D
A
0 X
0 1
X 0
0 1
B
C
2 essential primes
X 1
0 1
0 1
1 1
D
A
0 X
0 1
X 0
0 1
B
C