## Slide 1: CDA 3103
Recitation 7 – MIPS: Strings and Procedures

## Slide 2: MIPS Register Conventions
Name | Register Number | Usage | Preserved on call?
$zero | 0 | The constant value 0 | n.a.
$at | 1 | Reserved for assembler | n.a.
$v0-$v1 | 2-3 | Values for results and expression evaluations | No
$a0 - $a3 | 4-7 | Arguments | No
$t0 - $t7 | 8-15 | Temporaries | No
$s0 - $s7 | 16-23 | Saved | Yes
St8 - $t9 | 24-25 | More temporaries | No
$k0-$k1 | 26-27 | Reserved for operating system | n.a.
$gp | 28 | Global pointer | Yes
$sp | 29 | Stack pointer | Yes
$fp | 30 | Frame pointer | Yes
$ra | 31 | Return address | Yes

## Slide 3: MIPS and Strings
So far, we’ve seen mostly instructions for manipulating integers
Many programs also deal with strings
Strings are tricky because they don’t have a fixed length
  Ascii characters are 1 byte (8 bits)
  Java characters are 2 bytes (16 bits), also called halfword

## Slide 4: Load from memory
All load into end of register, pad with 0’s if necessary
Load byte (8 bits)
  lb register, address (all possible)
    treats the byte as signed
  lbu register, address (all possible)
    treats the byte as unsigned (eg. loading Ascii characters)
Load halfbyte (16 bits)
  Lh register, address (divisible by 2)
Load word (32 bits)
  Lw register, address (divisible by 4)

## Slide 5: Store to memory
sb register, address
  Stores last 8 bits of register into address
Sh register, address
  Stores last 16 bits of register into address divisible by 2
Sw register, address
  Stores full register into address divisible by 4

## Slide 6: Immediate Values
Load Immediate (16 bits or less)
  li register, constant
Load Immediate (greater than 16 bits)
  lui register, upper half of constant
  ori register, register, lower half of constant
Load Address (uses a label that must be resolved by the compiler)
  la register, label

## Slide 7: String Example
Find the number of spaces in a string
/* s contains the address of the string */
count = 0;
while (*s) {
if (*s++ == ’ ’) count++;
}

## Slide 8: String Example
Sometimes it helps to remove the higher-level structure as an intermediate step between a high-level language and assembly:
count = 0;
start: if (!(*s)) goto done;
if (!(*s == ’ ’)) goto skipinc;
count++;
skipinc: s++;
goto start;
done:

## Slide 9: String Example
Assume count is in $s0 and s is in $s1
li $s0,0 # count = 0
start: lbu $t0, 0($s1) # temp = *s
beq $t0,$zero, done # if *s == 0 goto done
li $t1,32 # temp2 = ’ ’
bne $t0,$t1, skipinc # if *s != ’ ’goto skipinc
addi $s0,$s0,1 # count++
skipinc: addi $s1,$s1,1 # s++
beq $zero,$zero, start # goto start
done:

## Slide 10: Additional Branches
branch if < 0 bltz $1,100 if ($1 < 0) PC = PC+4+400
branch if <= 0 blez $1,100 if ($1 <= 0) PC = PC+4+400
branch if > 0 bgtz $1,100 if ($1 > 0) PC = PC+4+400
branch if >= 0 bgez $1,100 if ($1 >= 0) PC = PC+4+400

## Slide 11: Supporting Procedures
Make parameters accessible ($a0-$a3)
Transfer control to the procedure (jal)
Get resources needed for the procedure
Perform the task
Make the result accessible ($v0-$v1)
Return to the calling program (jr $ra, where $ra = return address)

## Slide 12: Calling and Returning
To call a procedure:
  Place parameters in $a1 - $a3
  jal (jump and link)
    Stores return address (PC + 4) in $ra (31)
  Push register values onto stack (if they will be used)
To return:
  Place results in $v0 - $v1
  Pop register values off stack
  Jr $ra (jump register)
Notes: Why is it the procedure’s job (rather than the caller’s) to push and pop?
Note convention; $t registers not saved/restored; $s registers saved/restored

## Slide 13: Pushing onto Stack
$sp is top of stack
Stack grows from high memory addresses to lower memory addresses
Therefore, to put registers $s1 and $s2 on stack:
  addi $sp, $sp, -8
  sw $s1, 0($sp)
  sw $s2, 4($sp)

## Slide 14: Popping Registers
lw $s1, 0($sp)
lw $s2, 4($sp)
addi $sp, $sp, 8

## Slide 15: Example
int addfun(int a, int b) {
int res = a + b;
return res;
}
int t = 0;
for (int i=0; i<10; i+=2) {
t += addfun(A[i], A[i+1])
}

## Slide 16: Example – Procedure addfun
addfun:
add $v0, $a0, $a1
jr $ra

## Slide 17: Example - main
main:
la $s7, A #load starting location of array A
li $s0, 0 #start i at zero
li $s1, 0 #start res at zero
li $s6, 9 #for <10 comparison
loop:
sll $t0, $s0, 2 #multiply i by 4 for address
add $t0, $t0, $s7 #add base address of array to i
lw $a0, 0($t0) #load the value at i
lw $a1, 4($t0) #load the value at i+1
jal addfun #jump to the add fun function
add $s1, $s1, $v0 #add the result to t
addi $s0, $s0, 2 #increment i by two
bgt $s0, $s6, done #pseudoinstruction checks to see if i is greater than 9
j loop
done:

## Slide 18: Contents of an Object File
Header
Text segment (contains code)
Static Data segment (contains global static data)
Relocation information (internal labels)
  Instructions and data that depends on absolute addresses when the program is loaded into memory.
Symbol table (external labels)
  Labels defined in other object files
Debugging information

## Slide 19: Simplified Object File in MIPS
.text #start of text
main: #use main as label to start code
code goes here
.data #beginning of data segment
data goes here
.end #use for SPIM, not for MARS

## Slide 20: Specifying Data
Pseudoinstructions make data layout easier
  .word 100 #(4 bytes)
  .byte 25, 32, 41, 99 #(4 bytes)
  .asciiz “cat” #(4 bytes, including ‘\0’)
  .space 4 #(4 unspecified bytes)

## Slide 21: Example Object File (addfun)
.data
A: .word 12, 34, 67, 1, 45, 90, 11, 33
.text
.ent main
main:
addiu $sp,$sp,-24
sw $ra, 16($sp)
la $s7, A
li $s0, 0 #i
li $s1, 0 #res
li $s6, 9
loop:
sll $t0, $s0, 2
add $t0, $t0, $s7
lw $a0, 0($t0)
lw $a1, 4($t0)
jal addfun
add $s1, $s1, $v0
addi $s0, $s0, 2
bgt $s0, $s6, done j loop
done:
lw $ra, 16($sp)
addiu $sp, $sp, 24
jr $ra
.end main
.ent addfun
addfun:
add $v0, $a0, $a1
jr $31
.end addfun

## Slide 22: SYSTEM CALLS
  To request a service a program loads the system call code into register $v0 and the arguments into registers $a0 …$a3 (or $f12 for floating point values):
    print_int, the code is 1, the argument goes in $a0 = integer
    print_float, the code is 2, the argument goes to $f12 = float
    print_double, the code is 3, the argument goes into $f12=double
    print_string, the code is 4, the argument goes into $a0=string
22

## Slide 23: Additional Exercises - 1
Compute the value of the sum 1*2 + 2*3 + 3*4 + ... + 10*11, and store in register $t1
Additional instructions
  mult register, register (result is stored in $LO)
  mflo register (move result of $LO to register)

## Slide 24: Additional Exercises - 1
.data # variable declaration section
out_string: .asciiz "The result is:\n"
.text
.ent main
main: # indicates start of code
  li $t0, 1 # $t0 will be a counter; initialize to 1
  li $t1, 0 # $t1 will hold the sum
  li $t2, 10 # $t2 will hold loop limit
loop_top:
  bgt $t0,$t2,loop_end # exit loop if $t0 > 10
  addi $t3,$t0,1 # $t3 = $t0 + 1
  mult $t0,$t3 #Lo = $t0 * $t3
  mflo $t3 # $t3 = Lo (= $t0 * $t3)
  add $t1,$t1,$t3 # $t1 = $t1 + $t3
  addi $t0, 1 # increment counter
  b loop_top # branch to loop_top
loop_end: # print out the result string
  li $v0, 4 # system call code for printing string = 4
  la $a0, out_string # load address of string to be printed
  syscall # call operating system to # perform print operation
  # syscall will print from $a0
  # print out integer value in $t1
  li $v0, 1 # system call code for printing integer = 1
  move $a0, $t1 # move integer to be printed into $a0:
  syscall # call operating system to perform print
  .end main

## Slide 25: Additional Exercises - 2
.data
A: .word 0,1,2,3,4,5,6,7,8,9,
.text
.ent main
main:
la $s0, A
li $s1, 10
li $s2, 0 # the loop counter
li $s3, 0 # the result
loop:
sll $t0, $s2, 2
add $t0, $t0, $s0
lw $t0, 0($t0)
andi $t1, $s2, 1
bne $t1, $zero, loop_L1
add $s3, $s3, $t0
j loop_L2
loop_L1:
sub $s3, $s3, $t0
loop_L2:
addi $s2, $s2, 1
beq $s2, $s1, done
j loop
done:
li vo, 1
move $a0, $s3
syscall
.end main
What is the output being produced for this program assuming the answer being computed is stored in $s3?

## Slide 26: Additional Exercise - 2
$t1 = 0 for even number
$t1 = 1 for odd number
$s3 = 0 – 1 + 2 – 3 + 4 – 5 + 6 – 7 + 8 - 9

## Slide 27: Questions?